## Slide 1
PDS
Computer Vision
@ P. Siagian
Congestion
Network Performance
QoS :
https://www.youtube.com/@AmelOline/videos
https://github.com/siagianp
https://github.com/amelcharolinesgn2/IoT_simulator-mqtt-NodeRed
https://github.com/amelcharolinesgn2/Cloud-Infrastructures
https://github.com/amelcharolinesgn2/ClouD-Infrastructure-SISKA-2025
https://github.com/amelcharolinesgn2/Gyroscope-Sensor-Data-Accelerometer

## Slide 2: Outline
Bandwith
Congestion
Network Performance
Notes: https://study-ccna.com/cisco-bandwidth-command-clock-rate-speed/

## Slide 3
https://www.youtube.com/@AmelOline/videos
https://github.com/siagianp
https://github.com/amelcharolinesgn2/IoT_simulator-mqtt-NodeRed
PDS
Computer Vision
BANDWIDTH,THROUGHPUT,DAN KEBUTUHAN BANDWIDTH DALAM JARINGAN
BANDWIDTH,THROUGHPUT,DAN KEBUTUHAN BANDWIDTH DALAM JARINGAN
Bandwith

## Slide 5
Notes: https://forum.mikrotik.com/viewtopic.php?t=210807

## Slide 6
Bandwith
Bandwidth merupakan istilah yang digunakan untuk mengukur seberapa banyak informasi yang bisa dikirimkan oleh jaringan internet yang dihitung dalam satuan Bps atau bit per detik. Selain itu, kecepatan bandwidth juga ditunjukkan dalam satuan lain seperti Mbps (megabit) serta Gbps (gigabit) yang tergolong satuan miliaran Bps.
Bandwidth mempengaruhi seberapa cepat dan efektif media dalam melakukan transmisi seperti saat mengakses jaringan atau koneksi internet.
Semakin tinggi ukuran dan kecepatan bandwidth, maka semakin tinggi pula proses pengunduhan informasi di jejaring internet. Selain itu, bandwidth merupakan pengukuran yang dapat menunjukkan kapasitas maksimal dari tautan komunikasi kabel maupun nirkabel. Sehingga bisa juga digunakan untuk mengukur lama waktu tertentu dalam proses pengiriman data melalui jaringan internet.
Jumlah bandwidth yang dibutuhkan = Jumlah Perangkat (user) × Batas Maksimal Bandwidth untuk Setiap Perangkat.
Rumah ada 5 pengguna dengan masing-masing 2 perangkat laptop dan handphone dengan rincian sebagai berikut:
3 pengguna dengan 6 perangkat = pengguna berat yang memerlukan bandwidth dengan kapasitas 120 Kbps.
1 pengguna dengan 2 perangkat = pengguna sedang dengan kebutuhan bandwidth 80 Kbps.
1 pengguna dengan 2 perangkat = pengguna ringan dengan kebutuhan bandwidth 50 Kbps.
Cara menghitung bandwidth yang ideal untuk di rumah tersebut adalah:
(6x500 Kbps) + (2x300 Kbps) + (2x120 Kbps) = 3.840 Kbps atau 3,8 Mbps. Jadi sepesifikasi bandwidth pada modem yang diperlukan rumah tersebut supaya internet lancar adalah setidaknya 3,8 Mbps.
Menghitung Bandwidth
Kunjungi https://www.speedtest.net/
https://fast.com/id/
Notes: https://universe.roboflow.com/search?q=class%3Agourami
https://universe.roboflow.com/search?q=class%3Agourami
https://portal.fishial.ai/search/by-fishial-recognition
https://www.fao.org/fishery/en/culturedspecies/osphronemus_goramy/en
https://github.com/fishial/fish-identification/tree/main/train_scripts

## Slide 7
Throughput
Throughput merupakan istilah sebenarnya dari bandwidth yang diukur dengan satuan waktu tertentu dan pada kondisi jaringan tertentu yang digunakan untuk melakukan transfer file dengan ukuran tertentu.
Bila bandwidth adalah jumlah bit yang dapat dikirimkan dalam satu detik, throughput lebih menggambarkan tentang bandwidth aktual hingga jaringan internet tertentu yang digunakan untuk mengunduh suatu file dengan ukuran tertentu.
Notes: https://github.com/ahmadafif-codaff/anmik
https://github.com/buananetpbun/Mikrotik-Bandwidth-Monitoring-Script
Login-Hotspot-Dengan-QR-Scan-Barcode https://github.com/buananetpbun

## Slide 8
Satuan bandwidth diukur dengan satuan bps. Semakin besar bandwidth yang dimiliki oleh jaringan, semakin besar juga data yang dapat ditampung. Namun sebaliknya, semakin kecil bandwidth yang dimiliki, semakin kecil juga data yang bisa ditampung sehingga koneksi atau proses pengiriman data menjadi lebih lambat.
Memang bandwidth digunakan untuk mengetahui transaksi data yang dilakukan, namun tidak berarti bandwidth menjadi satu-satunya alat yang bisa berpengaruh pada kinerja jaringan. Sebab, masih banyak faktor yang bisa mempengaruhi transmisi data, seperti jiter, latency, paket boss, dan lain-lain.

## Slide 9
Kinerja throughput
Throughput memiliki cara kerja yang bervariatif karena bersinggungan langsung dengan tingkat lalu lintas jaringan, jumlah pengguna, latensi, dan masalah jaringan lainnya.
Umumnya, throughput memiliki cara kerja yang dapat diukur dalam bit per detik (bps), kilobit per detik (Kbps), megabit per detik (Mbps), atau gigabit per detik (Gbps). Berikut adalah beberapa point cara kerja throughput.
1. Bandwidth
Semakin besar bandwidth, potensi throughput juga semakin tinggi. Hanya saja yang perlu diketahui bahwa throughput selalu lebih kecil daripada bandwidth karena faktor jumlah pengguna, latensi dan lainnya.
2. Jarak
Jarak antara perangkat dan media transmisi seperti modem atau router dapat mempengaruhi throughput. Misalnya semakin jauh jarak, semakin besar kemungkinan penurunan kecepatan.
3. Interferensi
Gangguan elektromagnetik atau terhalang bangunan yang tinggi dapat mengurangi kualitas koneksi yang berdampak ke throughput secara langsung.
4. Protokol jaringan
Protokol yang digunakan untuk mengirimkan data dapat mempengaruhi efisiensi dan kecepatan transfer.
5. Beban jaringan
Semakin banyak perangkat yang menggunakan jaringan, semakin rendah throughput yang dapat diharapkan.
6. Kualitas layanan (QoS)

## Slide 10
Kinerja throughput
Several factors can influence throughput, including:
Bandwidth: Bandwidth is the maximum capacity of a network connection to transfer data. Higher bandwidth typically enables higher throughput. However, bandwidth is only a potential rate, and the actual throughput could be lower due to other factors.
Latency: Higher network latency can reduce throughput because it takes longer for data packets to travel across the network.
Packet loss: When data packets fail to reach their destination, the sending device often needs to resend them, which can lower the overall throughput.
Network congestion: When many data packets are trying to travel over the network simultaneously, it can lead to congestion and a decrease in throughput.
Hardware and infrastructure: The performance and efficiency of network hardware, such as routers and switches, can impact throughput.
Notes: https://www.kentik.com/kentipedia/latency-vs-throughput-vs-bandwidth/

## Slide 11
Bandwidth | Throughput
Bandwidth adalah data maksimal yang dapat ditransmisikan melalui koneksi internet sepanjang waktu. | Throughput lebih pada nilai data yang sesungguhnya dalam transmisi dan proses disisi network.
Bandwidth berkaitan dengan teori kecepatan maksimal dari koneksi. | Sedangkan Throughput adalah gambaran sebenarnya dari kecepatan data yang sedang berlangsung.
Bandwidth dapat dimulai dari bit /detik (bps). | Throughput dimulai dari bit /detik (bps) atau paket /detik (pps).
Notes: https://www.rumahweb.com/journal/throughput-adalah/

## Slide 12
Kinerja throughput
Jika bandwidth merupakan batas maksimal data yang bisa ditampung, maka throughput adalah data yang asli atau sebenarnya yang ada di dalam transmisi tersebut.
Sebagai contoh, ketika menggunakan internet dengan bandwidth sebesar 5 Mbps, namun ingin mengunduh file dengan kecepatan sebesar 4,2 Mbps. Inilah yang termasuk ke dalam throughput. Maksudnya, throughput merupakan kecepatan asli dari transmisi yang dikirimkan. Throughput akan selalu lebih kecil dibandingkan dengan bandwidth.
Contoh lain yang juga bisa adalah ketika sedang terhubung ke internet dengan besaran bandwidth-nya sebesar 4 Mbps. Ketika ingin mendownload file yang memiliki kapasitas 12 MB, ternyata file tersebut telah ter-download dalam waktu 12 detik. Lalu berapa throughput-nya? Jawabannya adalah 12/6 yang hasilnya 2 Mbps.
Untuk itu, bila Anda hendak berlangganan cloud server, pastikan telah tersedia paket cloud server dengan bandwidth yang cukup besar, misalnya 10 Gbps. Melansir dari Server Mania dan forum Web Hosting Talk, penyedia layanan cloud server rata-rata memberikan bandwidth hanya sebesar 1 Gbps. Besaran bandwidth ini pun sudah cukup cepat. Sehingga bila ada penyedia layanan cloud server yang mampu memberikan bandwidth dengan besaran 10 Gbps, maka proses unggah dan unduh data akan sangat cepat.

## Slide 13
Kinerja throughput
Throughput adalah aliran bps atau mbps pada jaringan internet yang diberikan oleh alat transmisi seperti router/modem berdasarkan sumber internet kepada perangkat client. Aliran throughput sangat relatif dan realtime sesuai keadaan dilapangan, artinya bahwa jika Anda sewa paket internet 100 Mbps, namun kenyataannya ketika di testing download file dan hanya berkisar 20 Mbps, maka itu adalah throughput.
Throughput tidak dapat lebih besar dari bandwidth, namun bisa lebih kecil dari bandwith. Apabila ingin dianalogikan secara lebih sederhana, maka bandwidth adalah pipa dan air adalah throughput.
Fungsi Throughput
throughput adalah aliran data atau traffic internet yang sesungguhnya dari alokasi bandwidth yang diberikan provider internet atau provider hosting. Secara umum, fungsi throughput adalah sebagai berikut:
1. Indikator kinerja
Berkaitan dengan informasi kecepatan dan efisiensi suatu sistem jaringan. Bagian ini sangat berguna untuk menentukan seberapa besar keuntungan dari penggunaan sumber daya internet yang dapat dimanfaatkan.
2. Alat perbandingan
Memungkinkan perbandingan antara berbagai sistem atau jaringan berdasarkan kecepatan, latensi dan seterusnya.
3. Dasar optimasi
Memberikan informasi dan identifikasi area yang dapat ditingkatkan untuk meningkatkan kinerja sistem.

## Slide 14: RouterOS Virtual Labs
https://forum.mikrotik.com/viewtopic.php?t=99658
Tujuan
Tujuan dari penelitian ini adalah untuk memberikan teknologi yang dapat memonitoring populasi dan pertumbuhan ikan dan melakukan penghitungan objek otomatis dengan memanfaatkan teknologi frame video. Petani budidaya ikan dapat monitoring untuk melakukan perlakuan yang lebih baik, seperti pengendalian kepadatan, menentukan jumlah pemberian pakan, dan jumlah yang wajar pakan membantu mengurangi polusi air dan memastikan pertumbuhan ikan yang cepat dan sehat.

## Slide 15
Notes: https://forum.mikrotik.com/viewtopic.php?t=99658
https://github.com/gns3/gns3-gui/releases
https://forum.mikrotik.com/viewtopic.php?t=99658
https://github.com/cs-uob/COMS20012/blob/master/docs/lectures/2025/Week%205%20-%20Security%20protocols%20and%20Private%20Network.pptx

## Slide 16
Notes: https://github.com/cdhtlr/MikroTik-Speedtest
https://github.com/cdhtlr/MikroTik-Speedtest
15.02
Sedang diputar
MikroTik Ookla Speedtest Based Failover part 1 - Router Setup

## Slide 17: MIKROTIK PORT SCANNER / ROUTER OS PORT TESTER
@echo off
title ROUTEROS PORT TESTER BY BNT
:Loop
echo.
echo =================================
echo -= ROUTEROS PORT TESTER BY BNT =-
echo =================================
echo.
set /p ip="Enter IP Address: "
echo.
echo PORT INFO:
echo - 8291 / Winbox
echo - 80 / WWW Webfig http
echo - 443 / WWW-SSL Webfig https
echo - 8728 / API
echo - 8729 / API-SSL
echo - 21 / FTP
echo - 22 / SSH
echo - 23 / Telnet
echo - 3128 / Open proxy
echo - 8080 / Open proxy
echo - 53 / DNS
echo - 2000 / Btest Server
echo.
echo Try for Scaning Port Please Wait...
echo.
PortCheck %ip% 8291,80,443,8728,8729,21,22,23,3128,8080,53,2000
echo.
IF %ERRORLEVEL%==1 echo - WARNING!! Open ports found, danger from attack!
echo - Please change your default port to another port
echo.
echo Scan Port Complete..
echo.
pause
cls
goto loop
Notes: https://github.com/buananetpbun/mikrotik-port-scanner

## Slide 18
Congestion
Congestion merupakan sebuah kondisi yang terjadi pada jaringan komunikasi dimana terlalu banyak paket yang datang pada sebuah subnet yang menyebabkan kinerja jaringan menjadi turun.
Faktor yang dapat mempengaruhi terjadinya Congestion :
Trafik yang masuk mendekati batas maksimal.
Kinerja perangkat router yang lambat dalam melakukan queuing buffer, updating table, dan sebagainya.
Buffer pada router yang dibatasi.
Congestion

## Slide 19
QoS
Quality of Services: Metode pengukuran yang bertujuan untuk menentukan kemampuan sebuah jaringan pada kelas-kelas tertentu yang dalam hal ini contohnya seperti aplikasi jaringan, host atau perangkat router dengan tujuan memberikan layanan jaringan yang lebih baik dan maksimal.

## Slide 20
QoS
Quality of Services
Bandwidth
Throughput
Jitter
Packet Loss
Latency

## Slide 21
Bandwidth
Bandwidth merupakan kapasitas atau lebar frekuensi yang dilewati oleh sinyal dalam media transmisi dengan satuan waktu bit per second (bps).

## Slide 22
Throughput
Kemampuan atau kecepatan transfer data yang sebenarnya dalam suatu jaringan ketika terjadi proses pengiriman data dengan satuan waktu bit per second (bps).
Kategori | Throughput | Indeks
Bad | 0-388 kbps | 0
Poor | 388-700 kbps | 1
Fair | 700-1200 kbps | 2
Good | 1200 kbps-2,1 Mbps | 3
Excelent | >2,1 Mbps | 4
Standarisasi Penilaian QoS (TIPHON)

## Slide 23
Jitter
Variasi waktu kedatangan paket data. Ketika paket data dikirim oleh pengirim dalam waktu secara bersamaan, namun kedatangan paket data tersebut bisa jadi tidak bersaaman.
Kategori | Jitter | Indeks
Poor | 125 - 225 ms | 1
Medium | 75 – 125 ms | 2
Good | 0-75 ms | 3
Perfect | 0 ms | 4
Standarisasi Penilaian Jitter (TIPHON)

## Slide 24
Packet Loss
Parameter yang menggambarkan suatu kondisi yang menunjukkan jumlah total paket data yang hilang dari pengirim ke penerima.
Standarisasi Penilaian Packet Loss (TIPHON)
Kategori | Packet Loss | Indeks
Poor | > 25% | 1
Medium | 12-24% | 2
Good | 3-14% | 3
Perfect | 0-2% | 4

## Slide 25
Latency
Total waktu tunda suatu paket data dari satu titik ke titik lain yang menjadi tujuannya.
Standarisasi Penilaian Latency (TIPHON)
Kategori | Packet Loss | Indeks
Poor | > 450 s | 1
Medium | 300 – 450 s | 2
Good | 150 – 300 s | 3
Perfect | < 150 s | 4

## Slide 26: Network Performance
  Bandwidth and Throughput
  Sources/Definitions of latency, jitter and loss
Network Performance

## Slide 27: Network properties
Latency
  Network Delays – fixed and variable
Jitter
  Variation in Delay: causes and impact
Throughput
  Bandwidth/Capacity: actual/available
Losses
  Packets drops, link and device failures, loops

## Slide 28: Latency & Jitter

## Slide 29: Reality Check
GOLDEN RULE
Information propagation IS NOT instantaneous
It is not possible for EVERY user to share the
EXACT same state at EVERY instance

## Slide 30: Impact on the Shared Experience
Host A
Host B
Host C
Notes: Illustration of Consistency issues by having three different hosts illustrating casual consistency with differences in the updates of an avatar. The host B is the owner of the avatar. In host A, there is a slight delay but then the avatar synchronizes by apparently moving faster than in Host B. The same concerning Host C, where the delay is even greater than in A.

## Slide 31: Overview of the Challenge
Mental Model
Senses
Muscles
Local Host
Network
Access
Human
System
Network
Human Brain
Devices
Internal Processing
Local Processing
Network Processing
The total processing time must not exceed the interactive threshold which is determined by Gameplay

## Slide 32: Latency and Jitter : Single Host
Application
System Model
Input
Simulation
Rendering
1
2
3

## Slide 33: Latency and Jitter : Networked Host
Application
System Model
Input
Simulation
Rendering
Network
Link
Physical
Internet
1
2
3
4
5

## Slide 34: Latency and Jitter : Client and Server
Server Application
Application
System Model
Input
Simulation
Rendering
Network
Link
Physical
Internet
1
2
3
5
6
Simulation
4

## Slide 35: Latency and Jitter : Single Host
Application
Input
Simulation
Rendering
Device
Display
Path A
Notes: Figure 10.1 (Top)

## Slide 36: Latency and Jitter : Client and Server
Client Application
Network
Link
Physical
Input
Simulation
Rendering
Device
Display
Server Application
Simulation
Physical
Link
Network
Path C
Path D
Path B
Notes: Figure 10.1 (Bottom)

## Slide 37: Latency : Network Perspective
Handler
Routing Table
Input Queues
Output Queues

## Slide 38: Latency : Network Perspective
Handler
Routing Table
Input Queues
Output Queues
Latency
Latency
Latency
Notes: Sources of latency:
Input queue : Queuing latency
Processing and error bit checking
Output queue : Queuing latency

## Slide 39: Network Delay : 4 Components
Sender
Router
Handle
Receiver
Router
Router
Transmission
Delay
Propagation
Delay
Queuing
Delay
Handling/Processing
Delay
Notes: Figure 10.2

## Slide 40: How do loss and delay (latency/lag) occur?
packets queue in router buffers
  packet arrival rate to link exceeds output link capacity
  packets queue, wait for turn
A
B
packet being transmitted (transmission delay)
packets queueing (queueing delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 41: Four sources of packet delay
1. nodal processing:
  check bit errors
  determine output link
A
B
propagation
transmission
nodal
processing
queueing
2. queueing:
time waiting at output link for transmission (can also be incurred at input to router, waiting for processing)
depends on congestion level of router

## Slide 42: Delay in packet-switched networks
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing
Note: s and R are very different quantities!

## Slide 43: A note on Queueing delay
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite!

## Slide 44: Total delay
dnodalproc = processing delay in the node (router)
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
  = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs
dtotal = dnodalproc+ dqueue+ dtrans+ dprop

## Slide 45: “Real” Internet delays and routes
What do “real” Internet delay & loss look like?
Traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 46: Real Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
Three delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic
link

## Slide 47: Traceroute Command
Man pages will give you the full options that can be used with traceroute
Example below specifies the time to wait ‘w’ for a response before giving up (5secs default), the number of queries ‘q’ to send (3 default), and max number of hops ‘m’ to reach destination (30 default)
traceroute -w 3 -q 1 -m 16 test.com

## Slide 48: Jitter
Jitter is: Variation in packet delay
Causes
  Variation in packet lengths -> different transmission times
  Variation in path lengths -> no fixed paths in the Internet
Jitter is caused by the technology of the Internet
  Routers are capacity bound and demand on routers changes rapidly
  Some link layers (notably wireless) are shared medium so transmitters will conflict

## Slide 49: Jitter
Sender
Receiver
Client A sends at
fixed intervals
Client B receives at
irregular intervals
Sometimes packets
arrive after interval deadline
Notes: Figure 10.4

## Slide 50: Variance of inter-packet arrival times
Interpacket arrival time
Frequency of occurrence
Correct
spacing
Gaussian distribution
Observed distribution

## Slide 51: Latency and Jitter : Network Perspective
Sender
Receiver
Internet
Regular Timing
Jittered Timing
Network Latency
Transmission Delay : time it takes to put a packet on the outgoing link
Propagation Delay : time it takes for the packet to arrive at destination

## Slide 52: Difference: Jitter and Latency
Latency and Jitter affect streams of packets travelling across the network

## Slide 53: Network Latency Estimate
ClientA
ClientB
TA0
TA1
TB0
TB1
Network Latency Estimate = ((TA1 – TA0) - (TB1 – TB0))/2
Clock Offset Estimate = (TB0 - TA0) – Network Latency Estimate
Notes: Figure 10.6

## Slide 54: Network Jitter Estimate
Sender
Receiver
TR0
TR1
TS0
TS1
Jitter Estimate = (TR1 – TR0) - (TS1 – TS0)
Jitter Moving Averagei = a x Jitter Estimatei + (1-a) x Jitter Moving Averagei-1
where 0 < a < 1
Notes: Figure 10.4

## Slide 55: Throughput & Loss

## Slide 56: Network Bandwidth/Capacity
Bandwidth is a shared resource
At local level we share the wireless or share a home or office router
However probably, the bottleneck is likely to be upstream to our ISP
ISP have intra-ISP bottlenecks
The destination site (BBC, Facebook) might have inbound capacity limits

## Slide 57: Loss
Another GOLDEN RULE
Packet Loss is a Good Thing
It is the Internet’s defence against failure
Dropping packets (hopefully) causes senders
(processes or users) to rate-limit

## Slide 58: Loss : Network Perspective
Handler
Routing Table
Input Queues
Output Queues
Loss
Notes: Queue is full, packet is dropped

## Slide 59: Packet loss
queue (aka buffer) preceding link has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)

## Slide 60: Throughput : Network Perspective
Throughput : number of bits per time of unit

## Slide 61: Throughput : Network Perspective
Throughput : number of bits per time of unit
Potential Loss and Increased Delay

## Slide 62: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)
server sends bits
(fluid) into pipe

## Slide 63: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
link on end-2-end path that constrains end-2-end throughput, i.e., the smallest/narrowest link
bottleneck link

## Slide 64: STATE OF THE INTERNET

## Slide 65: Bandwidth and Latency: Wired
Broadband is now common in homes
  500Kbps – 1Gbps
  Depends on technology (twisted-pair v. optical)
Offices have always been different
  1Gbps Ethernet, switched (not shared) is common
  Outbound varies enormously
Low Latency

## Slide 66: Bandwidth and Latency: Wireless
2G
  Don’t try, run web or sms-based applications!
3G / 4G
  3G: ~2.4Mbps
  4G: 100Mbps – 1Gbps
802.11a-n, ac
  b: 11 Mbps
  g: 54 Mbps
  n: 74 Mbps
  ac: 150Mbps
Latency is moderate-poor: its shared bandwidth

## Slide 67: Effect of distance on throughput and download times
Based on (Leighton, 2009)

## Slide 68
https://www.youtube.com/@AmelOline/videos
https://github.com/siagianp
https://github.com/amelcharolinesgn2/IoT_simulator-mqtt-NodeRed
https://github.com/amelcharolinesgn2/Cloud-Infrastructures
https://github.com/amelcharolinesgn2/ClouD-Infrastructure-SISKA-2025
https://github.com/amelcharolinesgn2/Gyroscope-Sensor-Data-Accelerometer