## Slide 1
PDS
Computer Vision
@ P. Siagian
https://www.youtube.com/@AmelOline/videos
https://github.com/siagianp
https://github.com/amelcharolinesgn2/IoT_simulator-mqtt-NodeRed
https://github.com/amelcharolinesgn2/Cloud-Infrastructures
https://github.com/amelcharolinesgn2/ClouD-Infrastructure-SISKA-2025
https://github.com/amelcharolinesgn2/Gyroscope-Sensor-Data-Accelerometer
Cisco Quality of Service

## Slide 2: What is Quality of Service
Quality of service is the key term to represent the set of requirements which a user (person or software component) wants to impose to his traffic.
Multiple mechanisms are available to fulfill these requirements.
Notes: b

## Slide 3: Why do we need them ?
Together, they provide tools that will allow us to define which action needs to be taken in case of congestion.
Understanding where they fit, what they exactly do, and how they work together do is necessary to:
  Correctly design and deploy QoS
  Monitor its activity
  Troubleshoot potential issues
Notes: The most common issue when it comes to QoS is bad design. Typical issues from customers:
They want to use ‘QoS’ or ‘Shaping’ or ‘LLQ’, instead of having requirements for their traffic
They want QoS mechanisms to work the way they think they should work, instead of how they were designed

## Slide 4
T
X
R
I
N
G
Wire
LLQ
Class Gold
Class Silver
Shaper
Policer
WRED
Scheduler
Classification
Queues
Notes: Packets come in
They are classified first.
Then if there are buffers left on the tx-ring and no packets in the queue, they are moved on the ring and from there will get to the wire (FIFO).
If not the queuing algorithm decides in which queue they will go.
If the queues are full, one packet will be dropped. Might be the one coming in, might be another one depending on the results of the WFQ algorithm.
If packets are present in the queues, the scheduler takes the next one according to the configured algorithm:
LLQ first.
Then the other queues according to the weight assigned to them.
To prevent LLQ from starving other classes, a policer is applied to drop packets if we reach the maximum configured rate
WRED does earl random drops in the queues to prevent TCP synchronisation
A shaper can replace the tx-ring if we want to whole thing to be lower that the wire speed
The shaper can be assigned directly to a queue as well.

## Slide 5
show policy-map interface
Ethernet0/0
Service-policy output: parent
Class-map: class-default (match-any)
4983 packets, 240814 bytes
5 minute offered rate 0 bps, drop rate 0 bps
Match: any
Traffic Shaping
Target/Average Byte Sustain Excess Interval Increment
Rate Limit bits/int bits/int (ms) (bytes)
4000000/4000000 25000 100000 100000 25 12500
Adapt Queue Packets Bytes Packets Bytes Shaping
Active Depth Delayed Delayed Active
- 0 4 240 0 0 no
Service-policy : child
Class-map: one (match-all)
575 packets, 10435 bytes
5 minute offered rate 0 bps, drop rate 0 bps
Match: ip precedence 5
Match: dscp default (0)
Queueing
Strict Priority
Output Queue: Conversation 136
Bandwidth 256 (kbps) Burst 6400 (Bytes)
(pkts matched/bytes matched) 0/0
(total drops/bytes drops) 0/0
Notes: So here is how the QoS we applied at the entrance of the Nightclub would look like when configured on the router.
The command used to display this is ‘show policy-map interface’, which is your number one troubleshooting tool when working on QoS related problems.
Colors match the ‘toon character’ performing the related task.
Already notice two counters, packets (pink) and pkts matched (yellow), where on represents the customer Anna saw (that is: all of them), while the other were queued by Bob (only when entrance was full)

## Slide 6
Class-map: two (match-all)
254 packets, 16743 bytes
5 minute offered rate 2000 bps, drop rate 0 bps
Match: any
Match: dscp 1
Queueing
Output Queue: Conversation 137
Bandwidth 512 (kbps) Max Threshold 64 (packets)
(pkts matched/bytes matched) 2/0
(depth/total drops/no-buffer drops) 0/0/0
Class-map: class-default (match-any)
1 packets, 60 bytes
5 minute offered rate 0 bps, drop rate 0 bps
Match: any
Queueing
Flow Based Fair Queueing
Maximum Number of Hashed Queues 128
(total queued/total drops/no-buffer drops) 0/0/0
exponential weight: 9
class Transmitted Random drop Tail drop Minimum Maximum Mark
pkts/bytes pkts/bytes pkts/bytes thresh thresh prob
0 3/452 0/0 0/0 20 40 1/10
1 0/0 0/0 0/0 22 40 1/10
2 0/0 0/0 0/0 24 40 1/10
3 0/0 0/0 0/0 26 40 1/10
4 0/0 0/0 0/0 28 40 1/10
5 0/0 0/0 0/0 30 40 1/10
6 0/0 0/0 0/0 32 40 1/10
7 0/0 0/0 0/0 34 40 1/10
rsvp 0/0 0/0 0/0 36 40 1/10

## Slide 7
QoS Models

## Slide 8: QoS Service Models
These are global, high level framework describing how QoS can be applied in a network.
Three services models:
  Best Effort
  Integrated Services
  Differentiated Services
Notes: Let’s quickly explain the first two, and spend some more time on the last one.

## Slide 9: QoS Model #1: Best Effort
First come, first served basis
Network’s behavior:
  Treats all traffic the same and on a first come, first served basis.
Drawbacks
  Delivers data if it can, with no assurances of reliability, delay bounds, or throughput. So basically no QoS ;)

## Slide 10: QoS Model #2: Integrated Services
Dynamic allocation of resources
Network’s behavior:
  Applications requests a specific level of service before starting to send data.
Drawbacks
  Requires explicit signaling through protocol (RSVP)
  Overhead in network services, scalability issues.

## Slide 11: QoS Model #3: Differentiated Services
Flows are aggregated in the network
Network’s behavior:
  Small numbers of aggregated flow follow the behavior implemented on each hop (‘Per Hop Behavior’).
Drawbacks
  Needs standardized policies to ensure end-to-end services
Notes: The most popular model, let’s look at how we standardized those policies to make it work end to end.

## Slide 12: DiffServ Architecture
Network Boundaries: Traffic Conditioner Block
  Incoming traffic is classified and can be conditioned (metered, delayed, dropped)
  Is assigned to an aggregate flow matching a behavior. This is done by marking it with a DiffServ Code Point (DSCP).
Network Core: Per Hop Behavior
  Traffic is forwarded/dropped according to the Per Hop Behavior corresponding to its DiffServ Code Point.
Notes: DiffServ Domain: on portion of network controlled by one authority where DiffServ is applied as QoS Service Model

## Slide 13: DiffServ Architecture
TCB in Cisco IOS
Class-Based Policing and Shaping
MQC-Based Classification and Marking
PHB in Cisco IOS
LLQ & WRED

## Slide 14: Per Hop Behavior
Defines the “Externally observable forwarding behavior” of a DiffServ node.
The DiffServ model associates the standard behavior of a participating node to the DSCP of the packets.
Some convention are used to ensure consistent usage of DSCP values across networks.
Notes: Defines the “Externally observable forwarding behavior” of a DiffServ node.
=> loss percentage, delay, jitter, drop precedence

## Slide 15: IP Precedence Field
“An independent measure of the importance of this datagram.”
8 values, meaning is now merely historical.
Defined in RFC 791 (Internet Protocol)

## Slide 16: DiffServ Code Points (DSCP) values
RFC 2474 redefines the TOS byte into DSCP values
6 bits = 64 values
DS-compliant nodes map a codepoint to a particular forwarding treatment or PHB.

## Slide 17: Per Hop Behavior
Can be split in 4 types:
Default PHB: 0
Class Selector PHB: IP Precedence
Assured Forwarding PHB: AF
Expedite Forwarding PHB: EF

## Slide 18: Per Hop Behavior
Default PHB:
  DSCP Value 000000, maps to IP Precedence 0
Class Selector:
  DSCP Value xxx000, maps to IP Precedence dec(xxx)
  Values of 110000 and 111000 should always have preferential treatment to preserve common values of routing traffic (precedence 6 and 7)
Notes: Do small IP Prec to DSCP exercise on the white board.
DSCP Precedence
101000 (Prec 5)
010000 (Prec 2)
56 (111000 => Prec 7)
48 (110000 => Prec 6)
(100000 =>32) Prec 4

## Slide 19: Per Hop Behavior
Assured Forwarding PHB:
  Guaranteed Bandwidth + Extra if available
  4 classes (af1, af2, af3, af4)
  3 drop probability values per class
  DSCP Value aaadd0, maps to 4 classes (aaa) and 3 drop probability (dd)
Expedite Forwarding PHB:
  Minimum departure rate (minimum delay)
  Guaranteed Bandwidth + Drop if excess (Policed)
  DSCP Value 101110
Notes: Another exercise on white board:
DSCP name Binary Decimal
AF21 (010010) (18)
(AF33) 011110 (30)
(AF42) (100100) 36
EF 101110 46

## Slide 20: Review Questions
Name the three QoS Models.
Which one of them involves the use of RSVP ? Why ?
What does DSCP stand for ?
To which type of PHB do those belong:
  101000
  101110
  010110
Which PHB class would you use for voice traffic ?
Notes: Answers:
Best Effort, Integrated Services, Differentiated Services
Integrated Services. Because we need a protocol to allow application to reserve bandwidth before using it.
Differentiated Services Code Point
101000 = class selector (Prec 5), 110010 = EF (not af52 ! Only 4 AF classes), 010110 Assured Forwarding (af23)
Expedite Forwarding (need delay guarantee)

## Slide 21: References
Cisco IOS – The Differentiated Services Model
  http://www.cisco.com/warp/public/cc/pd/iosw/prodlit/difsf_ds.htm
DiffServ - The Scalable End-to-End QoS Model
  http://www.cisco.com/en/US/partner/tech/tk543/tk766/technologies_white_paper09186a00800a3e2f.shtml
RFC 791 – Internet Protocol
RFC 2474 - Definition of the Differentiated Services Field (DS Field) in the IPv4 and IPv6 Headers
RFC 2475 - An Architecture for Differentiated Services
RFC 2597 - Assured Forwarding PHB Group
RFC 2346 - An Expedited Forwarding PHB
Notes: Cisco IOS 12.1(5)T and later versions comply with the core DiffServ RFCs.

## Slide 22: MQC

## Slide 23: What is MQC
MQC stands for Modular QoS CLI
Defined in EDCS 137373
Implements the DiffServ model
Basically: this is how you should configure Quality of Service on Cisco Routers.
class-map match-all one
match ip precedence 5
match dscp default
class-map match-all two
match any
match dscp 1
class-map match-all three
match protocol gnutella
!
policy-map test
class one
priority 100
class two
bandwidth 300
class three
drop
class class-default
police 75000 5000
fair-queue
!
interface Ethernet0/0
ip address 10.48.77.104 255.255.255.0
service-policy output test
!

## Slide 24: Why was MQC developed ?
Provide a platform-independent CLI for configuring QoS on Cisco platforms.
Use standard commands to define a QoS function or a general behavior.
  Defines the syntax and semantics
Move burden of complexity away from customers, who see functional innovation.
  Hides differences in algorithms or hardware implementation
  No platform specific commands

## Slide 25: How MQC Works: 3 Steps
Class-map – To define traffic classes (global config).
Policy-map – To associate policies/actions with each class of traffic (global config).
Service-policy – To attach policies to interfaces (logical or physical), in input or output direction (inteface config).
Note: MQC does not equate to CBWFQ. CBWFQ is a queuing mechanism that can be configured via MQC.
http://www.cisco.com/univercd/cc/td/doc/product/software/ios122/122cgcr/fqos_c/fqcprt8/qcfmdcli.htm

## Slide 26: MQC: Step 1 – Class-map
Creates a named traffic class
Specifies the packet-matching criteria need to be part of the class.
If more than one criteria, class-map can be ‘match-all’ or ‘match- any’. Default is match all.
A class named ‘class-default’ is always present, It matches packets that didn’t match a user-defined class.
class-map <match-(all|any)> <class name>
match <criteria>
match not <criteria>

## Slide 27: MQC: Step 2 – Policy-map
Named object representing a set of policies that are to be applied to a set of traffic classes:
  Ex: Minimum bandwidth guaranteed, maximum rate,…
Classes need to be defined first (except class-default)
  policy-map <map-name> class <class-map-name-1> <policy-1> <policy-n>
  class <class-map-name-n> <policy-n>
  class class-default
  <policy-default>
Notes: Class-map was defining classes, here we define what we do with them.

## Slide 28: MQC: Step 3 – Service-policy
Attach the previously created policy-map to an interface
Apply it to either input or output traffic
Interface can be physical :
  Main interface
Or logical :
  Subinterface, PVC, DLCI, Tunnel, Virtual-Template, Dialer, Multilink.
service-policy <output|input> <policy-name>

## Slide 29: MQC: Step 3 – Multiple policies
Input : Only on same level peers, ex:
  Valid: 3 different policies on 3 subinterfaces
  Invalid: 1 policy on main, 1 on a subinterface
Output: Only 2 levels, ex:
  Valid: 1 policy on main, 1 on a subinterface
  1 policy on main, 1 on PVC
  Invalid: 1 policy on main, 1 subinterface, 1 on PVC
Recent IOS should complain if invalid configuration attempted.
Notes: Applying the service policy is not as trivial as I may seem. Here are some restricions:
Today, there are various logical interfaces where a QoS service policy can be attached: ATM PVC/FR DLCI, sub-interface and main-interface. One can attach a service policy to all of the above three interfaces, however there is no need to support such an attachment today. We allow only the following combination of service policies and every other combination should be blocked with proper error messages to the user. The combos that are valid are: Input direction ---------------- Today, one can attach a service-policy at all three logical interface. The fix will be to allow service-policy attachment to only one logical interface. However, one should be able to attach service-policy to multiple logical interfaces which are peers (for eg attaching service policy to each of the ATM pvcs/FR dlcis is ok) but not to logical interfaces that are not peers (for eg attaching a service-policy to the main interface and a sub-interface should be blocked). Output direction ----------------- Today, one can attach a service-policy at all three logical interfaces. However, we support only service-policy at no more than 2 logical interfaces simultaneously. For eg we can support a service-policy attached to a pvc and a service-policy attached to a main-interface. But we do not support a service-policy attached to pvc and one attached to the sub-interface and one attached to the main-interface. The following combinations are valid: pvc(dlci) and main-interface sub-interface and main-interface The following combinations are blocked: pvc(dlci) and sub-interface pvc(dlci) and sub-interface and main-interface

## Slide 30: MQC: Hierarchical Policies
One policy-map can be used inside another one. The parent is the one applied to the interface.
Availability and number of levels depends on heavily on platform.
Often used with two levels: Shaper in parent, Queues in child, so the shaper can trigger the backpressure.
  policy-map child
    class http
    bandwidth <BW>
    class ftp
    policy-map parent
    class class-default
    shape average <CIR>
    service-policy child
Notes: More about parent shaper and queuing in the next sections

## Slide 31: Review Questions
What are the three steps when creating a QoS configuration with MQC ?
Can I have a service policy on my Fa0/0.1 and another one on my Fa0/0.2 ?
I created parent and child hierarchical policies, which one should I apply to my interface ?
MQC allows you to hide complexity from the end-user, can you see any disadvantage in this ?
Notes: Class-map definition
Policy-map definition
Service-policy on the interface
Yes and no
Yes in input
Yes in output
Parent
Sometimes, HW limitation are hidden by MQC, and end-users may try to configure unsupported/unrealistic QoS implementations on their router

## Slide 32: Lab 1: MQC
Configure a class-map to match telnet traffic
Configure a policy-map marking telnet traffic with precedence 5
Apply the policy-map on the ethernet interface
Notes: R1-eth-R2-serial-R3
R1: IOU Pagent to pre-configure
R2/R3: IOU 12.3 latest
Configure a class-map to match telnet traffic
Configure a policy-map marking telnet traffic with precedence 5
Apply the policy-map on the serial interface between R2 and R3, outgoing direction.
R1 flows used here:
1 flow to port 23, TOS 0
(1 flow TOS 0)
(1 flow TOS 6)

## Slide 33: Classification

## Slide 34: Classification
QoS component that makes the distinctions between packet streams.
Fundamental in QoS: without classification, all packets would be treated the same way.
Linked to the match CLI keyword, within a class-map
Exact possibilities depend on HW/SW revisions, but IOS can generally match on Layer 2, Layer 3, Layer 4, and even sometimes on payload information.

## Slide 35: Classification options
Here are the most common packet characteristics that we can match to asssign traffic to classes:
IP Precedence / DSCP
  Often the only one used in Core, since traffic is usually marked with either DSCP or Prec at the Edge.
MPLS Exp
  Equivalent to IP Prec but in MPLS networks.
Access-lists
  Very flexible up to Layer 4 information

## Slide 36: Classification options (2)
4. CoS (ISL/802.1q)
  Class of Service, usually in switches and router/switches, matches on L2 information.
5. DE bit, CLP bit
  Also layer 2 but for WAN. Discard Eligibility for Frame-Relay, Cell Loss Priority for ATM
6. Qos-group
  Special field internal to a router, set by the router itself without affecting the packet.
Notes: QoS group is usually set on input and reused for output classification.

## Slide 37: Classification options: NBAR
NBAR
- Network Based Address Recognition.
- Feature that allows matching on Layer 4+ packet information.
- Uses the match protocol statement in the class-map (not all match protocol use NBAR, but most do).
- Use show ip nbar port-map to show all supported protocols in your IOS release.
Note: not to confuse with NBAR protocol discovery, provided by the same feature but used to analyse traffic received on an interface, nothing to do with classification from a QoS point of view.
Notes: - Identifies to which high-level protocol a packet belongs. Goes beyond traditional classification and handles dynamically assigned UDP and TCP ports.
- The engineering documents refer to NBAR as a Stateful Inspection Language Engine (StILE), which is a high-level language for describing packets. At initialization, this language is reduced to a state graph. This state graph can be thought of as a flow chart instructing the router how to classify a packet.
- Each node in the graph will examine some bytes in a packet and use that information to produce a pointer to the next node.
- StILE supports several types of nodes, including:
  Decision nodes – Jump subnodes analyze a part of the packet that is 8 bits or less in length, while range subnodes analyze a value that is between the limits of some large range with an upper and lower limit.
  Decision update nodes – Alter the state graph during execution. E.g. StILE may identify the TCP port number that will be used for the H.225 control channel of a VoIP call and save it to the state graph to perform further analysis for that channel.

## Slide 38: NBAR: Supported Protocols
http://www.cisco.com/univercd/cc/td/doc/product/software/ios122/122cgcr/fqos_c/fqcprt1/qcfclass.htm#xtocid2010224
ToS
Byte
Source
IP Addr
Dest
IP Addr
IP Packet
TCP/UDP Packet
Src
Port
Dst
Port
Data Packet
Sub-Port/Deep Inspection
egp
exchange
kerberos
secure-nntp
smtp
gre
finger
l2tp
notes
snmp
icmp
ftp
ldap
novadigm
socks
ipinip
secure-ftp
secure-ldap
ntp
sqlnet
ipsec
gopher
netshow
pcanywhere
ssh
eigrp
http
pptp
pop3
streamwork
bgp
secure-http
sqlserver
secure-pop3
syslog
cuseeme
imap
netbios
printer
telnet
dhcp
irc
nfs
realaudio
secure-telent
dns
secure-irc
nntp
rcmd
tftp
vdolive
xwindows
napster
citrix

## Slide 39: NBAR Example: HTTP Classification
Extended Inspection: NBAR looks for an HTTP-specific signature in ports beyond well-known TCP port 80
router(config-cmap)#match protocol http ?
  host host-name-string -- Match Host Name
  url url-string -- Match URL String
  mime MIME-type -- Match MIME Type
HTTP Clients
Router X
Router Y
HTTP Server
Responses to HTTP GET
HTTP GET Request
Match protocol http: www.cisco.com/en/US/products/sw/iosswrel/ps5187/products_command_reference_chapter09186a008017cf0e.html#1112789
HTTP GET request contains Host/URL string
HTTP responses may be further classified by MIME-type
Notes: Slide from Tim McSweeney
When specifying a URL for classification, include only the portion of the URL following the
www.hostname.domain in the match statement. For example, for the URL
www.cisco.com/latest/whatsnew.html, include only /latest/whatsnew.html.
Host specification is identical to URL specification. NBAR performs a regular expression match on the
Host field contents inside an HTTP GET packet and classifies all packets from that host. For example,
for the URL www.cisco.com/latest/whatsnew.html, include only www.cisco.com.
For MIME type matching, the MIME type can contain any user-specified text string. A list of the
Internet Assigned Numbers Authority (IANA)-supported MIME types can be found at:
ftp://ftp.isi.edu/in-notes/iana/assignments/media-types/media-types
In MIME type matching, NBAR classifies the packet containing the MIME type and all subsequent
packets, which are sent to the source of the HTTP GET request.
29056

## Slide 40: Common Classification
Since 12.1(2)T, classification of packets is done at the same place for all features (twice: input and output).
Advantages:
  Classification policy-map counters incremented all the time, even without congestion
  Reduces CPU impact of ACLs by checking once per class, not once per feature.
  Allows for faster lookup of packet headers since the values are cached.
Class-map: one (match-all)
5715 packets, 107435 bytes
5 minute offered rate 140 bps, drop rate 0 bps
Match: ip precedence 5
Match: dscp default (0)

## Slide 41: Classification with Tunnels
IP
Since 11.3T, TOS Byte is copied to the tunnel or GRE IP header that encapsulates the inner packet. Previously, those bits were set to zero.
IP
Data/TCP/…
Data/TCP/…
GRE
T
O
S
T
O
S
T
O
S

## Slide 42: Classification with Tunnels
From 12.1(5)T (12.2(2)T on 2600 and 3600 series) introduced a new command:
qos pre-classify
Classification can now be done based on original port numbers and based on source and destination IP addresses, even when applied on Physical:
Original IP
Data/TCP/…
GRE header
Carrier IP
Notes: While it is ok to match on TOS bits since they are copied, matching on other IP Header field is not that easy => qos pre-classify

## Slide 43: Classification with Tunnels
Router(config)#interface tunnel0
Router(config-if)#qos pre-classify
Supported on Tunnel, Virtual-template, Crypto-map for :
  Generic Routing Encapsulation (GRE)
  IP in IP (IPIP) tunnels
  Layer 2 Tunneling Protocol (L2TP)
  Layer 2 Forwarding (L2F)
  Point to Point Tunneling Protocol (PPTP)
  IPSec.
http://www.cisco.com/warp/customer/105/qostunnel.html
http://www.cisco.com/univercd/cc/td/doc/product/software/ios122/122newft/122t/122t2/ftqosvpn.htm

## Slide 44: Classification with Tunnels
Policy on Tunnel – No pre-classify:
Policy on Physical – pre-classify:
Match on the Pre-Tunnel Header:
Original IP
Data/TCP/…
GRE header
Policy on Physical – No pre-classify:
Match on the Post-Tunnel Header:
Data/TCP/…
GRE header
Carrier IP
Carrier IP
Original IP

## Slide 45: Classification: Order of Operation
Input Common Classification
Input Access Lists
Input Marking (Class-Based Marking or CAR)
Input Policing (Class-Based Policing or CAR)
CEF or Fast Switching
Input Path

## Slide 46: Classification: Order of Operation
CEF or Fast Switching
Output Common Classification
Output Access Lists
Output Marking
Output Policing (via Class-Based Policer)
Traffic Shaping
Queuing (CBWFQ and LLQ) and WRED
Output Path

## Slide 47: Classification: Order of Operation
Input Classification (class-map)
Input QoS Actions (policy-map)
Output Classification (class-map)
Output QoS Actions (policy-map)
1
2
4
3
Routing
Ingress IF
Egress IF
service-policy input INPOLICY
service-policy output OUTPOLICY
Notes: This illustrate why any marking should be done in the INPUT policy-map and used in the OUTPUT policy-map, not both at the same time, because the classification done according to the class map is done in the steps 1 and 3 (dark green), and the QoS actions in 2 and 4 (orange) are done based on this classification AFTER. So if we re-mark traffic in the orange sections, the QoS action won’t be taken based on this re-marking since the traffic has already been classified. Even if marking is done before some other actions in the order of operation.

## Slide 48: Classification: Associated counters
Always incremented with common classification
Indicates the number of packets that matched the class requirements, not the packets that were queued.
Class-map: one (match-all)
5715 packets, 107435 bytes
5 minute offered rate 140 bps, drop rate 0 bps
Match: ip precedence 5
Class-map: two (match-any)
43693 packets, 2103334 bytes
5 minute offered rate 1856 bps, drop rate 20 bps
Match: ip precedence 2
Match: dscp default (0)
Notes: Show policy-map interface output

## Slide 49: Classification: Review Questions
What are two advantages of common classification ?
Which configuration keyword is directly associated with classification ?
I have a service-policy applied on a Tunnel interface, what should I configure to match on the original IP Header ?
Which feature is needed to match on a filename in a ftp get request ?
My classification counters are not increasing in the ‘show policy-map interface’ output, what could be the cause of this ? Try to find 3.
Notes: Less impact of ACLs
Accurate counters
Match
Nothing !
Pre-classify only needed if the policy is applied on the Physical and matching has to be done on pre-GRE ;)
NBAR
No traffic, no common classification and no congestion, service-policy applied to the wrong interface or in the wrong direction

## Slide 50: Marking

## Slide 51: Marking: What and Why
Marking adds, removes, or modifies a characteristic of a packet.
It is used to identify packets, either:
Locally: Only internal to the router (i.e. qos-group)
Network-wide: Packet itself is modified (i.e. DSCP)
P
R
E
C
5
IP Header
DATA

## Slide 52: Marking: How it works
Using Class-Based Marking
    Requires CEF to work.
    Packets are (re)marked using the set keyword.
Using a Policing mechanism
    Not the main purpose of the policer, but it is often used to (re)mark packet differently whether they conform or exceed the policer settings.
    Class-Based Policing or Committed Access Rate (CAR)

## Slide 53: Marking: What can be marked
Depending on the chosen marking method:
    IP Precedence
    DiffServ Code Point (DSCP)
    MPLS Experimental bits
    QoS groups
    ATM CLP bit
    Frame-relay DE bit
    IEEE 802.1Q or ISL CoS/priority bits (*)
    Discard-class
(*) Only for output policies on trunks

## Slide 54: Marking: CAR (pre-MQC)
Still often used because easy to configure, but MQC is cleaner and better.
vileplume(config-if)#rate-limit input dscp 45 800 800 800 conform-action ?
continue scan other rate limits
drop drop packet
set-dscp-continue set dscp, scan other rate limits
set-dscp-transmit set dscp and send it
set-mpls-exp-continue set exp during imposition, scan other rate limits
set-mpls-exp-transmit set exp during imposition and send it
set-prec-continue rewrite packet precedence, scan other rate limits
set-prec-transmit rewrite packet precedence and send it
set-qos-continue set qos-group, scan other rate limits
set-qos-transmit set qos-group and send it
transmit transmit packet

## Slide 55: Marking: Class-Based Policing
R2(config-pmap-c)#police 30000 conform-action ?
drop drop packet
exceed-action action when rate is within conform and conform + exceed burst
set-clp-transmit set atm clp and send it
set-discard-class-transmit set discard-class and send it
set-dscp-transmit set dscp and send it
set-frde-transmit set FR DE and send it
set-mpls-exp-imposition-transmit set exp at tag imposition and send
set-mpls-exp-topmost-transmit set exp on topmost label and send
set-prec-transmit rewrite packet precedence and send
set-qos-transmit set qos-group and send it
transmit transmit packet
<cr>
Similar to CAR
More Features (more fields can be marked)
Requires full MQC Configuration

## Slide 56: Marking: Class-based Marking
R2(config-pmap-c)#set ?
atm-clp Set ATM CLP bit to 1  since 12.2(4)T
cos Set IEEE 802.1Q/ISL class of service/user priority
discard-class Discard behavior identifier  since 12.2(13)T
dscp Set DSCP in IP(v4) and IPv6 packets
fr-de Set FR DE bit to 1  since 12.2(2)T
ip Set IP specific values
mpls Set MPLS specific values
precedence Set precedence in IP(v4) and IPv6 packets
qos-group Set QoS Group
Unconditional marking using the set command

## Slide 57: Packet Marking Notes
Packets are marked before queuing.
  Pete is changing the membership card after Bob decided which queue they go in, but before actually reaching the queue.
  Again, Bob’s decision relies only on what Anna decided.
CEF switching is required with set command in MQC.
Locally generated is special .
   Depends on platform
   EDCS-355797 (QOS Treatment of locally sourced traffic)

## Slide 58: Marking: Review questions
What are the two mechanisms to mark traffic in MQC ?
What are the associated keywords ?
I marked my important traffic with qos-group 1 and my peer router is matching on qos-group 1 to give it special treatment. Will this work ? Why ?
How can I fix this ?
In my output policy, I mark my voice traffic with Prec 5, and send Prec 5 to a high priority queue. Will my voice traffic be in the high priority queue ? Why ?
How can I fix this ?
Notes: Class-based policer and class-based marking
Police and Set
No, because qos-group is internal to the router
Mark the packet itself (DSCP, Precedence)
No, because queuing decision is done based on classification, and classification occurs before marking.
Mark the packet using an INPUT policy, and queue it in the OUTPUT policy

## Slide 59: Queuing and Scheduling
Notes: Bob’s role.
Let’s see which instruction you can give him to handle the flow of customers coming in.

## Slide 60
Congestion Management
Queuing + Scheduling = Congestion Management
  Buffering packets in queues
  Scheduling packets out of the queues
Outbound Packets
Scheduler
{
Packets in
Various Queues
Notes: Queuing :
  Congestion management entails the creation of queues, assignment of packets to those queues based on classification
Scheduling :
  Congestion management controls congestion by determining the order in which packets are sent from different queues out an interface based on packet priorities.
  Scheduling policy specifies how packets of different classes are served with respect to each other. Example scheduling policies include FIFO and WFQ.

## Slide 61: Definitions
The tx-ring, or TxQ, is buffer between the scheduler and the wire. It is always FIFO.
We will consider there is congestion when we receive backpressure signals.
Those signals can come from a full tx-ring (night club entrance full), or from a shaper (Nick tells Bob to start queuing, regardless of the status of the entrance)
scheduler
Software Q 1
Software Q n
Tx-ring
Wire signal
Notes: If a tx-ring is high, this will affect the delay of packets, and make QoS less effective.
On the other hand, a very low tx-ring will affect the CPU

## Slide 62: TxQ – How to see it ?
show controllers [int type] [int slot/subslot]
#sh int s0/1:0 | i str
Queueing strategy: fifo
#sh controllers serial 0/1:0 | i tx_limited
tx_limited = 0(128), errata19 count1 - 0, count2 – 0
#sh int s0/1:0 | i str
Queueing strategy: weighted fair
#sh control s0/1:0 | i tx_l
tx_limited = 1(2), errata19 count1 - 0, count2 - 0
Was the tx-ring reduced ?
(0 = default size)
Current size of the tx-ring
Notes: Exact output depends on interface controller (HW Chip used)
Applying QoS (other than FIFO) will automatically reduce the size of the tx-ring.
Notable exception are ATM interfaces, where the tx-ring needs to be manually decreased.

## Slide 63: Queuing and Dropping
Queuing/Scheduling have an associated dropping mechanism.
This can be simple tail drops (drop the next packet if queue is full), or more complex algorithm like fair drops (drops either the next packet or an already enqueued one)
There are also dropping mechanisms that are not linked to a Queuing/Scheduling algorithm, like WRED

## Slide 64: Queuing and Scheduling algorithm
FIFO Queuing
Legacy QoS (Priority Queuing, Custom Queuing)
Flow-based Weighted Fair Queuing
Class-based Weighted Fair Queuing
Low Latency Queuing
Notes: Algorithm is actually the instructions you gave to Bob

## Slide 65: FIFO queuing
Scheduling: First In, first out !
Drop: ‘tail-drop’
IOS: since ever
Switching Path: All
Performance Limitation: no
Many Drawbacks:
  Unfair, starvation, jitter (packet trains)
Forwarder
Driver

## Slide 66: Priority queuing (PQ)
Priority (ACL)
Forwarder
Low Priority
Normal Priority
Transmission Queue
Classification
Medium Priority
High Priority
Scheduling:
  FIFO within PQ.
  Preempt Priority among PQ’s
Drop: Tail-drop within PQ
IOS: since 7.0
Switching Path: all 11.2
High-priority traffic delay reduced but high risk of starvation for lower priority queues.
Notes: Deprecated.
Only here for the record.

## Slide 67: Custom Queuing (CQ)
Queue #0
Transmission Queue
Queue #1
Queue #2
Queue #3
Queue #4
Queue #5
Queue #6
Queue #9
Queue #10
Queue #11
Queue #12
Queue #13
Queue #14
Queue #15
Queue #7
Queue #16
Queue #8
Control Traffic
Custom (ACL)
Forwarder
Scheduling:
  FIFO within CQ, RR between up to 16 CQ’s
Drop: Tail-Drop within CQ
IOS: Since 9.0.
Switching Path: all
No starvation, but requires manual computation, and unreliable due to limitations of the algorithm.
Notes: Deprecated.
Sill sometimes used because it allowed two levels of priority queues
Byte-count based.
Queues were assigned byte counts, that would be decreased by the amount of bytes sent.
If only one byte left, it was still enough to send the packet, and move to the next queue (round robin).
Worst case:
Byte count of 2000: 1000 packet sent, 999 packet sent, 1000 packet sent => just sent 50% more than allocated !

## Slide 68
Fair-Queuing
Assume that each source-destination pair (conversation) can be distinguished and is stored in a logically distinct per-conversation queue.
Consider a hypothetical service discipline where one bit from each logical queue is served in a round-robin order.
This mechanism allocates bandwidth fairly, since at every instance in time, each conversation gets exactly its fair share of the trunk bandwidth
Emulation of a per-Flow TDM
Forwarder
Automatic Data Stream Classification
Driver

## Slide 69: Fair-Queuing
In practice there is a per packet scheduling (not bit-wise)
The objective is to achieve a per packet scheduling as close to the bit-wise fair-queuing as possible
Results in each flow getting its fair share of the bandwidth without being starved out (as happens with FIFO)
There are multiple implementations of WFQ: Flow-based WFQ (WFQ), Distributed WFQ (DWFQ), Class-based WFQ (CBWFQ), Distributed class-based WFQ (DCBWFQ), PXF-based WFQ,…

## Slide 70: Example
B2[300]
A3 [10]
A2[20]
B1[300]
A1[100]
Hence the resulting scheduling is:
t
100
70
60
50
0
A1
A2
A3
B2
B1

## Slide 71
Fair-queuing scheme with weight attribution allows certain flows to get relatively more bandwidth than others
On a per-packet basis (not per flow)!
Allocated bandwidth is PROPORTIONAL to the configured PRECEDENCE
  W = K/(Precedence+1) = WEIGHT
  K = 4096 until 12.0(5)T, 32384 after
RSVP and Pak-priority(*) packets have a special weight (4 and 128 respectively)
Flow-based Weighted FQ (WFQ)

## Slide 72: Checking Weight
router#show queue ATM 4/0.102
Interface ATM4/0.102 VC 0/102
Queuing strategy: weighted fair
Total output drops per VC: 1505772
Output queue: 65/512/64/1505772 (size/max total/threshold/drops)
Conversations 2/3/16 (active/max active/max total)
Reserved Conversations 0/0 (allocated/max allocated)
(depth/weight/discards/taildrops/interleaves) 1/32384/0/0/0
Conversation 2, linktype: ip, length: 58
source: 8.0.0.1, destination: 6.6.6.6, id 0x2DA1, ttl: 254, prot: 1
(depth/weight/discards/taildrops/interleaves) 64/32384/1505776/0/0
Conversation 15, linktype: ip, length: 1494
source: 7.0.0.1, destination: 6.6.6.6, id:0x0000, ttl: 63, prot: 255

## Slide 73
8 fixed system queues:
  LMI, ARP, PPP control, Routing protocol
2n dynamic queues (hashing)
  IP Flow = 109-bit string (6 fields) = {Sadd, Dadd, PID, Sport, Dport, 5-bit ToS}
  16 -> 4096, default is 256 (11.2)
x RSVP queues 0 -> 1000 [def: 0]
  Weight of RSVP flow with largest BW reservation = 4 (6 after 12.0(5)T)
WFQ: Per-Flow Sub queues

## Slide 74: WFQ: Per-Flow Sub queue
In theory, 1 Sub-queue per Flow (= conversation)
In practice, Flows are hashed in a set number of sub-queues (16 up to 4096)
router#sh int s 0
Input queue: 0/75/0 (size/max/drops); Total output drops: 10607
Queueing strategy: weighted fair
Output queue: 65/64/10607 (size/threshold/drops)
Conversations 3/5 (active/max active)
Reserved Conversations 0/0 (allocated/max allocated)

## Slide 75: Finish Time
Each packet is tagged with its Finish time in a virtual TDM system.
The scheduler selects the packets with the earliest finish time tag (thus the packet that leaves the virtual TDM the earliest)
"On the Efficient Implementation of Fair Queueing", Keshav, Berkeley, 1994
Notes: http://www.cs.cornell.edu/home/skeshav/book/slides/scheduling/ppframe.htm
Suppose, in each round, the server served one bit from each active connection
Round number is the number of rounds already completed
If a packet of length p arrives to an empty queue when the round number is R, it will complete service when the round number is R + p  finish number = R + p (independent of the number of connections)
If a packet arrives to a non-empty queue, and the previous packet has a finish number of f, then the packet’s finish number is f + p
Serve packets in order of finish numbers

## Slide 76: Weighted Fair Queuing
Classify packet to match a sub-queue (hashing)
Calculate the current round number (as in a bit-wise per-flow TDM)
Calculate the finishing time for each packet as it arrives. In WFQ, the FT will be calculated based on the round number, packet size and Weight.
The scheduler will serve packets from different queues based upon the Finishing Time (FT). The packet with the lowest FT will be the one to be sent to the transmit queue.
Notes: A hashing algorithm will put the traffic in a physical limited number of queues. The scheduler will serve the packets from different queues based upon the Finishing Time (FT). This way we get an implementation that doesn't work per flow but per packet. The packet with the lowest FT will be sent first to the transmit queue of the interface.
This is how the weight (W) is calculated :
W=K/(precedence +1)
and K=4096 or 32384.
The lower the weight, the higher the priority and the share of the bandwidth. Apart from the weight the length of the packet is also taken into account. The calculation of the FT is done like this :
If Flow F Active,
FT(Pfk+1) = FT(Pfk) + Size(Pfk+1) * W
Else,
FT(Pf0) = Now + Size(Pf0) * W
With Pfk being an already enqueued packet and Pf0 a first packet that comes into a queue.

## Slide 77: Computing Finish Time (FT)
The higher the IP Prec, the lower the weight, and the higher the priority and the share of the bandwidth.
We use weight and packet size to calculate FT like this :
If Flow F Active,
  FT(Pfk+1) = FT(Pfk) + Size(Pfk+1) * W
Else,
  FT(Pf0) = Now + Size(Pf0) * W
With Pfk being an already enqueued packet and Pf0 a first packet that comes into a queue. b
Notes: Remember weight :
W=K/(precedence +1)
and K=4096 or 32384.
How to compute the round number ?  when is NOW ?
FROM keshav :
Naively : round number = number of rounds of service completed so far
 what if a server has not served all connections in a round ? (i.e. round time is too short)
 what if new conversations join in halfway through a round ?
Redefine round number as a real-valued variable that increases at a rate inversely proportional to the number of currently active connections
Problem : iterated deletion
A server recomputes round number on each packet arrival
At any recomputation, the number of conversations can go up at most by one, but can go down to zero
 overestimation
Trick
  Use previous count to compute round number
  If this makes some conversation inactive, recompute
  Repeat until no conversations become inactive
(A connection is active if the last packet served from it, or in its queue, has a finish number greater than the current round number)

## Slide 78
FT(B2)=350+300
B2[300]
FT(A3)=120+10
A3 [10]
FT(A2)=100+20
A2[20]
FT(B1)=50+300
B1[300]
Hence the resulting scheduling is:
A1[100]
FT(A1)=0+100
t
100
70
60
50
0
Computing Finish Time FT
If Flow F Active, FT(Pfk+1) = FT(Pfk) + Size(Pfk+1) * W Else,
FT(Pf0) = Now + Size(Pf0) * W
A1 FT=100
A2 FT=120
A3 FT=130
B1 FT=350
B2 FT=650
Notes: WFQ does NOT schedule packets based on their arrival time (as would do FIFO).
WFQ does the following:
Packet arrival:
1. classify packet in its conversation queue
2. tag the packet with its finish round number:
The Finish round number is computed based on the following parameters:
- latest finish round number of the packet’s conversation
- packet size
Scheduling task:
Each time the wire is available, WFQ dequeues the packet with lowest finish round number and sends it on the wire

## Slide 79
Upon enqueue of a new packet,
IF the sum of all subqueues > Max-limit,
THEN, if the tail time of the new packet is > current system tail time, then the new packet is dropped else the system tail-time packet is dropped and the new one is enqueued
IF CDT < the sum of all subqueues < Max-limit,
THEN, if the new packet’s tail time > current system tail time then drop the new packet else enqueue the new packet
Exception: a packet classified into an empty sub-queue is never dropped
The packet precedence has no effect on the dropping scheme
Fair Dropping
Notes: There is a dropping mechanism associated with WFQ which is more complex than simple tail drop.

## Slide 80
Fair Drops example
CDT = 8, Max-Limit=14

## Slide 81
WFQ: CLI commands
fair-queue [congestive-discard-threshold 64 [1, 512] [dynamic-queues 256 [16, 4096] [reservable-queues]]] 0 [0, 1000]
holdqueue <max-limit> out
Optimised for minimizing jitter on low-speed links
Main limitation of WFQ is that is is resource intensive (maintaining a sorted list.)

## Slide 82
Software Implementation
Forwarder
Interface Congested?
WFQ Interface Queues
Transmission Queue
Yes
No
Always FIFO
Is TxAcc=0?
Upon sending, TxACC+=1
Packet stays in I/O
Pointer exchange

## Slide 83: Review Questions
What is the difference between a flow, a conversation, and a sub-queue ?
What is the maximum number of dynamic sub-queues we can configure ?
What is the main metric used when deciding which packet to send first ?
How does IP Precedence influence that decision ?
Notes: Flows are hashed into (256) conversations
Conversations are mapped to a queue 1-to-1, so we can reasonably say that a conversation = a queue.
4096
Finish Time
Influences the Weight (K/Prec+1) which is used to compute the Finish Time

## Slide 84: Class-Based WFQ
Same concept as WFQ
Here we will manually reserve bandwidth for pre-defined classes, which will result in a weight, compared to dynamic weight assigned dynamically created conversations with Flow-Based WFQ.
The higher the configured bandwidth, the lower the weight.
Exact conversion from bandwidth to weight is complex, and is done auto-magically by the router.

## Slide 85: Example of CBWFQ computation
WFQ type kbps/Prec Weight Arrival Times Finish Times
RSVP 4 0,20,40,50 4,24,44,54
OSPF/Pak 128 0,50 128,183
Class 1 200 kbps 4 5,10,15,20,25 9,14,19,24,29
Class 2 100 kbps 8 0,10,20,30 8,18,28,38
Class 3 50 kbps 16 5,25,45 31,41,61
flow 1 0 4096 100 4196
flow 2 0 4096 200 4296
flow 3 5 682 20 702

## Slide 86: CBWFQ Configuration
Class-based WFQ can only be configured via MQC.
To reserve bandwidth for a class, use the bandwidth keyword.
This sets the weight for all packets within that class.
Within a class where bandwidth is configured, queuing is FIFO !
policy-map cbwfq
class Data100k
bandwidth 100
class Sig50k
bandwidth 50
class class-default
fair-queue

## Slide 87: Bandwidth allocation
By default, the sum of all reserved bandwidth in a CBWFQ policy-map must be lower than 75% of the interface bandwidth
That interface bandwidth is defined by the bandwidth interface-configuration command, so this should be set correctly !
The 75% can be tuned using the max-reserved-bandwidth interface-configuration command
Defaults have changed with HQF

## Slide 88
Class Based WFQ
Scheduling based on Finish Time
Class #1
Class #2
Class #3
Class #4
Per class
(ACL)
Forwarder
Per flow
(hash)
Flow #2
Flow #3
Flow #1

## Slide 89: Available Bandwidth
router#sh queueing int atm 4/0.10
Interface ATM4/0.10 VC 0/101
Queueing strategy: weighted fair
[output omitted]
Available Bandwidth 1500 kilobits/sec
This can be seen in the show interface output. It is the difference between the sum of all reserved bandwidth and the maximum reservable bandwidth of the interface (by default 75% of the bandwidth)
Example :
ATM pvc SCR = 6M. 75% of 6M is reservable:
  .75 * 6000000 = 4500000
3M used by voice and data classes:
  4500000 - 3000000 = 1500000 bps
Available bandwidth is 1500000 bps.

## Slide 90: How Is Unused Bandwidth Allocated?
policy-map foo
class bar
bandwidth percent 30
class baz
bandwidth percent 60
With a 1 Mbps link:
  300 kbps is guaranteed to class bar.
  600 kbps is guaranteed to class baz.
  100 kbps is leftover for class-default.
  If class-default does not need it, unused 100 kbps is available for class bar and class baz.
  If both classes need it, they share it in proportion to configured rates i.e. 30:60 or 1:2.
Notes: LLQ and CBWFQ do not implement an absolute reservation. If a traffic class is not using its configured bandwidth, any unused bandwidth is shared among the other bandwidth classes.
If excess bandwidth is available, the excess bandwidth is divided amongst the traffic classes in proportion to their configured bandwidths. If not all of the bandwidth is allocated, the remaining bandwidth is proportionally allocated among the classes, based on their configured bandwidth.

## Slide 91: CBWFQ: The bandwidth command
Provides minimum guaranteed bandwidth.
Three ways to use it:
  bandwidth {kbps} – BW allocation as a bit rate. (12.0(5)T)
  bandwidth percent {value} – BW allocation as a percentage of the underlying link rate.(12.1(1))
  bandwidth remaining percent {value} – B/w allocation as % of bandwidth not allocated. (12.2T)
  Calculation for bandwidth percent changes per IOS version and there is a difference between 7500 and low-end. Check out :
  http://www.cisco.com/en/US/partner/tech/tk39/tk48/technologies_tech_note09186a00800fe2c1.shtml#understand
Notes: Note: The bandwidth command defines a behavior, which is a minimum bandwidth guarantee.
Not all Cisco router platforms use weighted-fair queueing as the underlying algorithm to implement
this behavior.

## Slide 92: CBWFQ: The Queue-limit command
The MQC queue-limit command applies only to CBWFQ classes configured with the bandwidth command.
It is the size of the queue.
Default queue-limit value varies with the platform. For low-end, the default value is often 64.

## Slide 93: Review Questions
If bandwidth is configured, which queuing is used within the class ?
What happens when bandwidth is configured in the class-default ?
You are trying to have three classes reserving 4 Megs, 2 Megs and 2 Megs on your 10 Megs Ethernet, but the router complains about not having enough bandwidth for that. What could be the reason ?
Which DiffServ PHB bandwidth could be linked to ?
Notes: FIFO
Class-default becomes FIFO and gets a weight matching the configured bandwidth.
This means all traffic in that class now has reserved bandwidth.
You need to increase the max-reserved-bandwidth to 80%
AF (assured forwarding – guaranteed minimum bandwidth)

## Slide 94: Low Latency Queuing (PQCBWFQ)
Bandwidth matches AF PHB. We need a mechanism for EF PHP that provides low delay guarantees.
So this should also implement both a minimum and a maximum bandwidth.
This is done simply by creating a class with a weight of zero and a built-in policer that prevents it from starving the other classes.
This is obviously used for traffic such as voice and real-time video
Notes: - A priority queue was introduced within the WFQ system as a fix for the pervasive voice problems seen by the customers. For more description on that problem please refer to the ddts CSCdm00717 and ENG-36555. There is a need now to support the use of that priority queue for ATM PVCs and also to provide a much richer set of classification criteria (for packets going into the priority queue). This documents describes how both these requirements will be met by introducing CLI support for the priority queue from within the CBWFQ modular CLI framework.
- This work will also provide the differentiated services expedited forwarding (EF) like functionality via the modular CLI CBWFQ framework. Packets going into the priority queue will get the EF class of service. CSCdm66986 will allow one to match packets based on the EF DSCP (diff-serv code point) via access-lists. So if the network elements/hosts set the EF DSCP, EF service will be available to those packets.

## Slide 95: Low Latency Queuing (PQCBWFQ)
Scheduling based on Finish Time
Class #1
Class #2
Class #3
Class #4
Per class
(ACL)
Forwarder
Per flow
(hash)
Flow #2
Flow #3
Flow #1
PQ

## Slide 96: CBWFQ vs LLQ
 | Bandwidth Command | Priority Command
Minimum bandwidth guarantee | Yes | Yes
Maximum bandwidth guarantee | No | Yes
Provides low latency | No | Yes

## Slide 97: Bandwidth vs Priority
During congestion, LLQ cannot use any excess bandwidth.
 | Congestion | Non-Congestion
bandwidth | Allowed to exceed the allocated rate | Allowed to exceed the allocated rate.
priority | Packets metered, token bucket. Excess packets are discarded. | The class can exceed its configured bandwidth (*)
Notes: (*) Exception is MLP, where the policer is active even without congestion.

## Slide 98: LLQ: The priority command
Reserves a minimum an maximum bandwidth
Two ways to use it:
  priority {kbps} – BW Allocated as a bit rate
  priority percent {value} – BW allocated as percentage of underlying rate (12.2(2)T)
Other parameter: burst (12.2(3)T)
  This is how you control the associated policer
  Default value is 200ms of the reserved bandwidth for the class
Only one LLQ !
  Multiple classes using priority will have to share the same queue.

## Slide 99: Review questions
What are the three keywords we can use to configure queuing within a class ?
What is the weight of class configured with the command ‘priority 100’ on a 2Mb/s interface ?
I have two delay sensitive traffic classes, voice and video, for which I use LLQ. Will my video streams affect the voice quality ?
I am using PQCBWFQ, everything was fine but recently the traffic increased slightly, and the voice quality dropped down to almost un-hearable. What could have happened ?
Notes: Bandwidth, Fair-queue, Priority
0 – LLQ is always 0
Yes, because there is only one LLQ even if configured in different classes in the same policy
You were using a lot of bandwidth for voice traffic, much more than what the LLQ was configured for.
Once the whole interface became congested, the built-in policer of the LLQ kicked in and voice traffic dropped down to the configured value.
(such situations should be avoided, it’s a bad design to send more LLQ traffic than the configured bandwidth.)

## Slide 100: Policing and Shaping

## Slide 101: Policing and Shaping
Both are control mechanisms to know when traffic conforms or exceeds the set contract
Policing: conform/exceed actions are set by the user!
Shaping: conform means packet is sent while exceed means that packet is delayed in a waiting queue

## Slide 102: Metering: the Token Bucket
Packets
arriving
YES: Conform
NO: Exceed
B - Burst size ( = Bc+Be)
p - Token arrival rate.
1 token = credit for 1 byte
Enough Credits?
p
Tokens
B
Overflow
Tokens
In practice, add an increment of Bc tokens every Tc ms
Notes: The token bucket accumulates token at the “Committed Rate” up to the burst level. When that happens the token overflows.
As a packet arrives if there is a matching token the packet is said to conform otherwise exceed.
Token comes in bytes.
The token size must match the packet size for a conform.
“Committed Rate” = increments of 8Kbits/milisec.

## Slide 103: Token Bucket
Bc tokens are added to the bucket every Tc ms
If bucket is full, new tokens are discarded
When a packet of n bytes arrives, n tokens are removed from the bucket and packet is transmitted
If fewer than n tokens are available, no tokens are removed from the bucket, and the packet is considered to be non-conformant.
  ‘non-conformant’ packets may be dropped, queued, marked, transmitted,…

## Slide 104: Shaping
Remote Sites
T1
Central Site
Frame Relay, ATM
128kbps
256kbps
512kbps
768kbps
T1
Result:
Buffering = Delay or Dropped Packets
When shaping, a packet considered ‘non-conformant’ will be queued.
The exact type of queuing depends on the configuration
This makes shaping a very good mechanism to trigger backpressure.
Notes: There are generally three reasons to implement traffic shaping:
1. High speed to low speed circuit mismatches. There are two possibilities here:
  The hub site has a T1 line into the cloud, while the remote site has a lower speed (56 Kbps). In this case, you need to rate-limit the hub site so that it does not exceed the remote side access rate.
  The hub site has a single T1 line into the cloud, while the remote sites also have a full T1 line into the cloud, connecting to the same hub site. In this case, you need to rate-limit the remote sites so as to not overrun the hub.
2. Oversubscription. For example, if the guaranteed rate on a permanent virtual circuit (PVC) is 64 Kbps and the access rate is 128 Kbps on both ends, it is possible to burst above the guaranteed rate when there is no congestion and fall back to the guaranteed rate when there is congestion.
3. Quality of Service. For implementing FRF.12 fragmentation or low latency queuing features for better quality of service to certain packet flows.

## Slide 105: Shaping parameters
Committed information rate (CIR) : This is the average rate of transmission (*)
Time interval (Tc) : Time interval between two replenishments of token bucket.
Burst size committed (Bc) : This is the number of bits added to the token bucket every Tc (*)
Burst size excess (Be) : Allow the token bucket to grow as deep as Be + Bc if not all Bc tokens are used in an interval. If Be>0, it is possible (but limited in time) to send more than Bc bits during a Tc (*)
(*) configurable through CLI
Notes: Therefore CIR = Bc/Tc
Drawing on whiteboard: throughput/time

## Slide 106: Example
Bc = 1M
CIR = 1Mbps
Time (s)
Rate (Mbps)
TC = 1s
1
2
3
1
2
Bc
Bc
interface rate = 2Mbps
Tc1
Tc2
Tc3
If there is continuous traffic, then on average we achieve a shaped rate of 1M (2M during 1/2s, every second = 1Mbps)
Notes: Let’s suppose a serial interface with 2Mbps of bandwidth
We are shaping at 1 Mbps (CIR).
If the Bc (number of token added in one interval) is 1Mbit, this means the Tc will be 1s

## Slide 107: Shaping: Selecting Bc and Tc
Selecting Values for data :
  Bc = CIR/8 or Tc = 125 ms *
Selecting values for voice :
  Bc = CIR/100 or Tc = 10 ms *
  Voice packets cannot tolerate a long delay
Larger Bc = Larger Tc, this can affect voice latency
* Since HQF, 4ms is supported everywhere
Notes: Supported values from 10 ms to 125 ms.
If a larger value is configured, Cisco IOS actually uses an internal value to ensure better stability.
Bc cannot be lower than 1000 bits
Since HQF, default should be 4ms for all traffic.

## Slide 108: Generic Traffic Shaping (pre-MQC)
Old way of configuring shaping
Queues for non-conformant packets were WFQ
CLI is the interface-configuration command :
Not seen anymore, replaced by MQC
(config-if)#traffic-shape rate <CIR> [<Bc> [<Be>]]
Notes: CIR is called here ‘mean rate’
Bc ‘sustained burst size’
Be ‘exceed burst size’

## Slide 109: Class-based Traffic Shaping
Same idea, but applied to a MQC Class
Two options:
  shape average – Bc every Tc normal shaping behavior
  shape peak – Bc+Be every Tc hardly ever used in practice
Percent option
  available since 12.2(13)T
shape {average | peak} {percent percent | cir}
[bc] [be]
Notes: Still have to find a use for peak shaping
Basically = shaping at a higher CIR than the configured one with a Be of zero.

## Slide 110: Class-Based Shaper: CLI
To specify the maximum number of buffers allowed on shaping queues, use the shape max-buffers command in class-map configuration mode.
(config)# policy-map SHAPING
(config-pmap)# class AF
(config-pmap-c)# shape average 1000000
(config-pmap-c)# exit
(config)# interface pos1/0/0
(config-if)# service-policy output SHAPING

## Slide 111: Class-Based Shaper: CLI
Router# show policy interface Serial 3/0
Serial3/0
output : parent
Class shaped
Weighted Fair Queueing
Output Queue: Conversation 267
Bandwidth 241 (kbps) Max Threshold 64 (packets)
(pkts matched/bytes matched) 3852/947384
(pkts discards/bytes discards/tail drops) 0/0/0
Traffic Shaping
Target Byte Sustain Excess Interval Increment Adap
Rate Limit bits/int bits/int (ms) (bytes) Active
241000 1928 7712 7712 32 964 -
Queue Packets Bytes Packets Bytes
Depth Delayed Delayed Active
41 3980 978872 3967 975686 yes
CIR
Bc
Be
Tc

## Slide 112: Class-based Shaper: Interactions
You can use a shaper with other features, like bandwidth (set, priority, bandwidth,…) in the same class.
Example: shape + bandwidth
  The class will have a minimum reserved bandwidth.
  The maximum usage when no congestion is defined by the shaper.
  Only makes sense if shape CIR >= bandwidth.
NB: Some exotic combinations may not make sense
Notes: Explain why BW>shape rate wouldn’t make sense
This is equivalent to Nick moving ot a particular queue

## Slide 113: Class-Based Shaper: Hierarchical
Very common setup.
Parent service-policy is shaping
Child is organizing the queuing behind it. Basically the class queues are replacing the shaping queues that are created when shaper is used in non-hierarchical way.
Only one level of shaping is allowed
In this case the shaper is creating the backpressure needed to start queuing, replacing the physical interface tx-ring. Very useful for things like PPPoE.
Notes: This is when Nick tells Bob to start queuing..
Ask why this can help with PPPoE

## Slide 114: Policing with CAR (pre-MQC)
Easy to configure, so we still see it
Configured directly on the interface, without MQC
rate-limit CR NB EB ...
CR: Equivalent of CIR
NB: Equivalent of Bc
EB: NOT Be, but Bc+Be (so EB >= NB)
Notes: Confusing parameters, don’t use the Shaper

## Slide 115: Policing with CAR
Usually we choose EB = 2 * NB.
If your packet size are bigger than EB (so bigger than NB also), those packets will be considered exceeding
Possible actions:
  Transmit: transmit the packet
  Drop: drop the packet
  Continue: go to the next rate-limit statement
  Set [x] and transmit: set [x] and transmit the packet
  Set [x] and continue: set [x] and continue to next statement

## Slide 116: Class-Based Policing
Benefits from MQC classification options
Configure in policy-map with police command
Allows multiple levels deep in hierarchical policy-map
Allows multi-action policers
BUT:
No continue option
No rate-limit acl

## Slide 117: Class-Based Policing: Options
1. Single rate, single bucket, two-color marker
  Same behavior as CAR
2. Single rate, dual bucket, three-color marker
Same as CAR + Violate action.
Here NB and EB are separated. Packets using NB bits conform, packets using EB exceed, and packets above EB violate.
police bps [burst-normal] [burst-max] conform-action action exceed-action action
police bps [burst-normal] [burst-max] conform-action action exceed-action action violate-action action
Notes: Dual Bucket / Three Color
Tb1 = actual amount of tokens in 1st bucket
Tb2 = actual amount of tokens in 2nd bucket
B = size of packet P
Packet P arrives :
If (Tb1 - B) >= 0
then {conform(P)
Tb1 = (Tb1 – B) }
else If (Tb2 – B) >= 0
then {exceed(P)
Tb2 = (Tb2 – B)}
else {violate(p)}

## Slide 118: Single rate, Dual Bucket, Three-Color Marker
NB
EB
Violate
Action
no
B tokens in E?
no
yes*
Exceed
Action
yes*
Conform
Action
Packet of B bytes arrives
B tokens in C?
* Token count decremented
Excess tokens
Tokens added
at every new
packet arrival
NB and EB are configured
independently
Notes: Assumptions :
1token per byte
Token buckets starts full at Tb1 = Tb2 = 1000.
A 550-byte packet arrives:
  Tb1 – 550 >=0  conform
  Tb1 = 1000 - 550 = 450 (Tb2 =1000)
The next packet arrives .25 seconds later:
  250 tokens are added to Tb1 (0.25 * 8000)/8)
  Tb1 = Tb1 + 250 = 700
If the next packet is 800 bytes :
  Tb1 – 800 < 0
  Tb2 – 800 >= 0 exceed
  Tb2 = Tb2 – 800 = 200
If the next packet arrives .40 seconds later :
400 tokens are added to Tb1 (.40 * 8000)/8)
Tb1 <= 1000 !  700 + 400 = 1000 + 100
Maximum size of Tb1 = 1000 100 tokens overflow to Tb2
Tb1 = 1000
Tb2 = 200 +100 =300
If the arriving packet is 1100 bytes :
Tb1 – 1100 < 0
Tb2 – 1100 < 0  violate

## Slide 119: Class-Based Policing: Options
3. Dual rate, dual bucket, three-color marker
  Similar as before except the excess bucket is also filled, using another rate (PIR)
  If the excess bucket isn’t big enough, packet violates. If it’s big enough but the normal bucket is not, packet exceeds (excess bucket is decremented), if normal bucket is big enough, packet conforms and BOTH buckets are decremented.
police {cir cir} [bc conform-burst] {pir pir} [be peak-burst] (+actions)
Notes: If (B > Tp(t))
Then violate(P)
Else If (B > Tc(t))
Then{exceed(P)
Tp(t) = Tp(t) – B}
Else{conform(P)
Tp(t) = Tp(t) – B
Tc(t) = Tc(t) – B}

## Slide 120: Dual Rate, Dual Bucket, Three-color Marker
Be
Bc
Tokens added at every new packet arrival
PIR (Be)
Violate
Action
yes
B tokens in C?
B tokens in P?
yes**
no
Exceed
Action
no*
Conform
Action
Packet of B bytes arrives
* Token count decremented
** Token count on both buckets decremented
CIR (Bc)
Notes: Tc token bucket – Updated at CIR value with each arriving packet. Bucket can contain up to conform burst (Bc) value.
Tp token bucket - Updated at PIR value with each arriving packet. Bucket can contain up to the peak burst (Be) value.
  Tc(t) = min(CIR * (t-t1) + Tc(t1), Bc)
  Tp(t) = min(PIR * (t-t1) + Tp(t1), Be)

## Slide 121: Dropping
Notes: Bob’s role.
Let’s see which instruction you can give him to handle the flow of customers coming in.

## Slide 122: WRED: What and Why
(W)RED stand for (Weighted) Random Early Drop
(W)RED is a dropping mechanism not associated with any type of queuing (unlike Fair Dropping)
Simple tail dropping has significant flaws:
  TCP synchronization
  TCP starvation
  High delay and jitter
  No differentiated drop
  Poor feedback to TCP
(W)RED makes most sense in TCP-heavy environments

## Slide 123
The issue of TCP Synchronization
Time
Queue Utilization
100%
Tail Drop
3 Traffic Flows Start at Different Times
Another Traffic Flow
Starts at This Point

## Slide 124: RED, WRED, Operation modes
RED comes in addition to whatever queuing is configured.
It can operate in three modes:
  No drop: not enough packets in the queue to start dropping
  Random drop: ideally we should drop here
  Full drop (= Tail drop): state we don’t want to reach
Weighted RED uses the same mechanism, but applies different parameters depending on IP Precedence or DSCP.

## Slide 125: WRED Parameters
Three parameters can be configured:
  Min Threshold: Queue size at which random drops start to occur. Must be large enough to allow link utilization to be maintained at an acceptable high level if traffic is bursty.
  Max Threshold: Queue size at which all packets are dropped. Ideal value depends on maximum average delay that can be tolerated.
  Mark Probability Denominator: Chance of dropping between Min Threshold and Max Threshold = 1/MPD
Router(config-if)#
random-detect {prec-based | dscp-based}

## Slide 126: Configuring WRED
interface Hssi0/0/0
ip address 200.200.14.250 255.255.255.252
random-detect
random-detect precedence 0 32 256 100
random-detect precedence 1 64 256 100
random-detect precedence 2 96 256 100
random-detect precedence 3 120 256 100
random-detect precedence 4 140 256 100
random-detect precedence 5 170 256 100
random-detect precedence 6 290 256 100
random-detect precedence 7 210 256 100
random-detect precedence rsvp 230 256 100
Each precedence can be separately configured

## Slide 127
WRED Service Profile Example
Packet Discard
Probability
1
Average
Queue
Size
Standard
Min
Standard
Max
Premium
Min
Premium
Max
Standard
Service
Profile
Premium
Service
Profile
Adjustable
Notes: When the probability starts increasing = Min Threshold
When it reaches 1 = Max Threshold (By default, max threshold is 2x min threshold)
Slope = Mark probability

## Slide 128
Data from a burst E1 (2.0 Mbps) courtesy of Sean Doran and Van Jacobson
RED was turned on Friday at 10:00 am. Link utilization goes up to 99%
Friday
Thursday
Benefits of RED

## Slide 129: Review questions
What is the difference between RED and WRED ?
Which traffic type gets the most benefit from Random Dropping ?
If you have configured WRED and still see tail drops, which parameters could you adjust to prevent them ?
How would you adjust them ?

## Slide 130: Segue Slide
Subtitle
Troubleshooting
AKA “How to read a show policy-map interface”

## Slide 131
show policy-map interface
Ethernet0/0
Service-policy output: parent
Class-map: class-default (match-any)
4983 packets, 240814 bytes
5 minute offered rate 230 bps, drop rate 0 bps
Match: any
Traffic Shaping
Target/Average Byte Sustain Excess Interval Increment
Rate Limit bits/int bits/int (ms) (bytes)
4000000/4000000 25000 100000 100000 25 12500
Adapt Queue Packets Bytes Packets Bytes Shaping
Active Depth Delayed Delayed Active
- 0 4983 240814 2 497 no
Service-policy : child
Class-map: one (match-all)
575 packets, 10435 bytes
5 minute offered rate 0 bps, drop rate 0 bps
Match: ip precedence 5
Match: dscp default (0)
Queueing
Strict Priority
Output Queue: Conversation 136
Bandwidth 256 (kbps) Burst 6400 (Bytes)
(pkts matched/bytes matched) 0/0
(total drops/bytes drops) 0/0
Notes: So here is how the QoS we applied at the entrance of the Nightclub would look like when configured on the router.
The command used to display this is ‘show policy-map interface’, which is your number one troubleshooting tool when working on QoS related problems.
Colors match the ‘toon character’ performing the related task.
Already notice two counters, packets (pink) and pkts matched (yellow), where on represents the customer Anna saw (that is: all of them), while the other were queued by Bob (only when entrance was full).
So the packets counter increments all the time (with Common Classification), while the other one increments only for:
- non CEF-switched packets (because you saw in IOS Arch that those were queued => counter incremented_
- CEF switched packets when tx-ring was full (thus congested)

## Slide 132
Class-map: two (match-all)
254 packets, 16743 bytes
5 minute offered rate 2000 bps, drop rate 0 bps
Match: any
Match: dscp 1
Queueing
Output Queue: Conversation 137
Bandwidth 512 (kbps) Max Threshold 64 (packets)
(pkts matched/bytes matched) 2/487
(depth/total drops/no-buffer drops) 0/0/0
Class-map: class-default (match-any)
15 packets, 60 bytes
5 minute offered rate 0 bps, drop rate 0 bps
Match: any
Queueing
Flow Based Fair Queueing
Maximum Number of Hashed Queues 128
(total queued/total drops/no-buffer drops) 0/0/0
exponential weight: 9
class Transmitted Random drop Tail drop Minimum Maximum Mark
pkts/bytes pkts/bytes pkts/bytes thresh thresh prob
0 15/1452 0/0 0/0 20 40 1/10
1 0/0 0/0 0/0 22 40 1/10
2 0/0 0/0 0/0 24 40 1/10
3 0/0 0/0 0/0 26 40 1/10
4 0/0 0/0 0/0 28 40 1/10
5 0/0 0/0 0/0 30 40 1/10
6 0/0 0/0 0/0 32 40 1/10
7 0/0 0/0 0/0 34 40 1/10
rsvp 0/0 0/0 0/0 36 40 1/10
Notes: CLASSIFICATION:
4983 packets, 240814 bytes -> packet classified as belonging to this class
5 minute offered rate 230 bps, drop rate 0 bps -> total rate (drops included) and drop rate for this class
SHAPER:
Parameters:
- 4000000/4000000 -> configured CIR
- 25000 -> Bc + Be in bytes (200000 bits)
- 100000 -> Bc in bits
- 100000 -> Be in bits
- 25 -> Tc
- 12500 -> Bc in bytes
Queue Depth 0 -> should match the number of packets queued (in child classes if parent shaper)
Packets/Bytes -> should match classification since they all go through the shaper
Packets/Bytes Delayed -> should match the total number of packets that have be queued (pkts/bytes matched) in child classes
Shaping Active -> if yes, backpressure triggered and packets are being queued (instant value)
Note: the shaper does not drop, it queues, and the queues drop.
Queuing (priority)
Classification counters: same as above
Strict priority -> indicates this is LLQ
Conversation -> number assigned to this class
Bandwidth -> reserved bandwidth
Burst -> Bc of the strict policer associated with the LLQ
(here 6400 bytes = 200ms * 256kbit/s = 1/5s * 32kbytes/s = 32000 bytes/5 = 6400 bytes)
Pkts/byte matched -> packets/byte queued here
Total/byte drops -> packets/byte dropped in this queue
Queuing (bandwidth)
Classification counters: same as above
Conversation -> number assigned to this class
Bandwidth -> reserved bandwidth
Max Threshold 64 -> size of the queue (remember, this is FIFO)
Pkts/byte matched -> packets/byte queued here
Depth/total drops/no-buffer drops -> number of packets in the queue right now, number of drops, number of drops, not due to algorithm or queue filled but lack of actual buffers in the router (means no QoS applied)
Queuing (fair-queue)
Classification counters: same as above
Flow Based Fair Queuing-> queuing method used here
Maximum number of Hashed Queues -> number of queues flows will be hashed to (128 is default, up to 4096 configurable)
Total queued/total drops/no-buffer drops -> same as above, except the first one showing the total number of packets queued in all dynamic fair-queues together.
WRED
Exponential weight: advanced WRED config parameter, not covered during this presentation
Class -> IP Precedence here. Could also be configured to DSCP
Transmitted pkts/bytes -> number of packets/bytes that went through WRED without being dropped
Random drop pkts/bytes -> number of packets/bytes dropped by the WRED algorithm, real early drops
Tail drop pkts/bytes -> number of packets/bytes dropped due to queue filled. Usually not desired, to reduce them you can
- Increase Mark Prob (drop more packets once Min is reached)
- Decrease Min threshold (start dropping sooner)
- Increase Max threshold (queue more, reach 100% drop later)
Minimum threshold -> number of packets in the queue at which we could start dropping
Maximum treshold -> number of packets in the queue at which we drop everything
Mark prob -> chance of packet between Min/Max to be dropped

## Slide 133: Case studies
These are more or less common QoS issues as reported by our customers.
Goal of the training it to force you to *think* about the possible causes using what we just learned today.

## Slide 134: Case study #1: Drops in show interface
‘my QoS is not working. I see drops in show int but nothing in show policy-map int’
Ethernet1/0 is up, line protocol is up (…)
Input queue: 0/75/0/0 (size/max/drops/flushes); Total output drops: 2945
Possible causes
QoS is not applied correctly => verify classification counters
Drops are not occurring at queuing level => verify hardware counters
Interface is not aware it is congested => verify shaper if any
  Are we shaping higher than the interface bandwidth ?
  Is our overhead accounted for ?
Notes: To verify classification counters, just check them in show policy-map interface. If they are not increasing, your qos is not applied, it’s a control plane issue.
Show controller or whatever platform specific command to look for drops due to transmission errors, drops alter down the asic path, etc…

## Slide 135: Case study #2: Jitter or delay
‘voice quality is bad, measurement shows high delay and/or jitter on the link’
It’s important, if you or your customer believes it’s QoS related, to isolate the node where delay occurs.
Possible causes
Queuing is the number one cause. The longer the queue, the higher the delay, and the higher the risk of jitter.
Is the priority traffic hitting a priority class ? If not, it HAS to, bandwidth classes provide NO guarantee of delay.
Is the priority ‘propagated’ ? Are packets treated as priority all the way down to the tx-ring
Is the tx-ring limited ? Large (default) tx-ring value voids the priority class. Same thing can be said of of shaper with large burst/tc.

## Slide 136: Case study #3: Class-default drops
‘I’m running lab tests, class-default is dropping way to soon, other classes are taking its bandwidth’
Show policy-map int will show class GOLD (30%) using 49.9%, class SILVER (30%) using 49.9% and class-default only gets 0.2%.
Possible cause
Fair-queue is used in the class-default, and test only send on data stream.
Class-default is using one of it’s 256 queues, with high weight, competing with GOLD and SILVER.

## Slide 137: Case study #4: Hierarchical policers
‘I’m using a policer in child and parent. Some packets are dropped outside of show policy-map interface’
Service-policy input: PARENT
Class-map: class-default (match-any)
506756 packets, 62837744 bytes
conformed 304414 packets, violated 200304 packets
Service-policy : CHILD
Class-map: Realtime-In (match-any)
253378 packets, 31418872 bytes
conformed 60987 packets, violated 92239 packets
Class-map: class-default (match-any)
253378 packets, 31418872 bytes
5 minute offered rate 81000 bps, drop rate 0 bps
Possible causes
Order of operation is the key here. What occurs first ?
Notes: Class real-time:
Total: 253378
Conformed: 60987
Violated: 92239
So 100152 packets are missing ?
Classification occurs first, so packets were classified in the CHILD before they were dropped in the parent.
200304 packets were dropped by the parent, most likely here ½ in each class so 100152. These are the ‘lost packets’.
Would it be the same with shaping ? No, shaping doesn’t drop, just queues in the child.

## Slide 138: Case study #5: QoS on GigabitEthernet
‘Using an output policy on my GigE, my classes are not receiving the bandwidth I configured’
sh policy-map int | i depth
(depth/total drops/no-buffer drops) 0/3587/0
sh policy-map int | i depth
(depth/total drops/no-buffer drops) 61/4244/0
sh policy-map int | i depth
(depth/total drops/no-buffer drops) 0/5167/0
sh policy-map int | i depth
(depth/total drops/no-buffer drops) 0/6004/0
sh policy-map int | i depth
(depth/total drops/no-buffer drops) 0/7251/0
sh policy-map int | i depth
(depth/total drops/no-buffer drops) 27/8274/0
Possible causes
Drops are occurring on input due to resources limitations
Output queues are too small and classes are ‘starving’:
  Tune your queue limits.

## Slide 139: Revision
Approved by Aleksandar Vidakovic (TAC Expert)
Last revision: October 26th 2008