## Slide 1: Network Behaviour & Impairments
PDS

## Slide 2: Network Performance
  Bandwidth and Throughput
  Sources/Definitions of latency, jitter and loss

## Slide 3: Network properties
Latency
  Network Delays – fixed and variable
Jitter
  Variation in Delay: causes and impact
Throughput
  Bandwidth/Capacity: actual/available
Losses
  Packets drops, link and device failures, loops

## Slide 4: Latency & Jitter

## Slide 5: Reality Check
GOLDEN RULE
Information propagation IS NOT instantaneous
It is not possible for EVERY user to share the
EXACT same state at EVERY instance

## Slide 6: Impact on the Shared Experience
Host A
Host B
Host C
Notes: Illustration of Consistency issues by having three different hosts illustrating casual consistency with differences in the updates of an avatar. The host B is the owner of the avatar. In host A, there is a slight delay but then the avatar synchronizes by apparently moving faster than in Host B. The same concerning Host C, where the delay is even greater than in A.

## Slide 7: Overview of the Challenge
Mental Model
Senses
Muscles
Local Host
Network
Access
Human
System
Network
Human Brain
Devices
Internal Processing
Local Processing
Network Processing
The total processing time must not exceed the interactive threshold which is determined by Gameplay

## Slide 8: Latency and Jitter : Single Host
Application
System Model
Input
Simulation
Rendering
1
2
3

## Slide 9: Latency and Jitter : Networked Host
Application
System Model
Input
Simulation
Rendering
Network
Link
Physical
Internet
1
2
3
4
5

## Slide 10: Latency and Jitter : Client and Server
Server Application
Application
System Model
Input
Simulation
Rendering
Network
Link
Physical
Internet
1
2
3
5
6
Simulation
4

## Slide 11: Latency and Jitter : Single Host
Application
Input
Simulation
Rendering
Device
Display
Path A
Notes: Figure 10.1 (Top)

## Slide 12: Latency and Jitter : Client and Server
Client Application
Network
Link
Physical
Input
Simulation
Rendering
Device
Display
Server Application
Simulation
Physical
Link
Network
Path C
Path D
Path B
Notes: Figure 10.1 (Bottom)

## Slide 13: Latency : Network Perspective
Handler
Routing Table
Input Queues
Output Queues

## Slide 14: Latency : Network Perspective
Handler
Routing Table
Input Queues
Output Queues
Latency
Latency
Latency
Notes: Sources of latency:
Input queue : Queuing latency
Processing and error bit checking
Output queue : Queuing latency

## Slide 15: Network Delay : 4 Components
Sender
Router
Handle
Receiver
Router
Router
Transmission
Delay
Propagation
Delay
Queuing
Delay
Handling/Processing
Delay
Notes: Figure 10.2

## Slide 16: How do loss and delay (latency/lag) occur?
packets queue in router buffers
  packet arrival rate to link exceeds output link capacity
  packets queue, wait for turn
A
B
packet being transmitted (transmission delay)
packets queueing (queueing delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 17: Four sources of packet delay
1. nodal processing:
  check bit errors
  determine output link
A
B
propagation
transmission
nodal
processing
queueing
2. queueing:
time waiting at output link for transmission (can also be incurred at input to router, waiting for processing)
depends on congestion level of router

## Slide 18: Delay in packet-switched networks
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing
Note: s and R are very different quantities!

## Slide 19: A note on Queueing delay
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite!

## Slide 20: Total delay
dnodalproc = processing delay in the node (router)
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
  = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs
dtotal = dnodalproc+ dqueue+ dtrans+ dprop

## Slide 21: “Real” Internet delays and routes
What do “real” Internet delay & loss look like?
Traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 22: Real Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
Three delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic
link

## Slide 23: Traceroute Command
Man pages will give you the full options that can be used with traceroute
Example below specifies the time to wait ‘w’ for a response before giving up (5secs default), the number of queries ‘q’ to send (3 default), and max number of hops ‘m’ to reach destination (30 default)
traceroute -w 3 -q 1 -m 16 test.com

## Slide 24: Jitter
Jitter is: Variation in packet delay
Causes
  Variation in packet lengths -> different transmission times
  Variation in path lengths -> no fixed paths in the Internet
Jitter is caused by the technology of the Internet
  Routers are capacity bound and demand on routers changes rapidly
  Some link layers (notably wireless) are shared medium so transmitters will conflict

## Slide 25: Jitter
Sender
Receiver
Client A sends at
fixed intervals
Client B receives at
irregular intervals
Sometimes packets
arrive after interval deadline
Notes: Figure 10.4

## Slide 26: Variance of inter-packet arrival times
Interpacket arrival time
Frequency of occurrence
Correct
spacing
Gaussian distribution
Observed distribution

## Slide 27: Latency and Jitter : Network Perspective
Sender
Receiver
Internet
Regular Timing
Jittered Timing
Network Latency
Transmission Delay : time it takes to put a packet on the outgoing link
Propagation Delay : time it takes for the packet to arrive at destination

## Slide 28: Difference: Jitter and Latency
Latency and Jitter affect streams of packets travelling across the network

## Slide 29: Network Latency Estimate
ClientA
ClientB
TA0
TA1
TB0
TB1
Network Latency Estimate = ((TA1 – TA0) - (TB1 – TB0))/2
Clock Offset Estimate = (TB0 - TA0) – Network Latency Estimate
Notes: Figure 10.6

## Slide 30: Network Jitter Estimate
Sender
Receiver
TR0
TR1
TS0
TS1
Jitter Estimate = (TR1 – TR0) - (TS1 – TS0)
Jitter Moving Averagei = a x Jitter Estimatei + (1-a) x Jitter Moving Averagei-1
where 0 < a < 1
Notes: Figure 10.4

## Slide 31: Throughput & Loss

## Slide 32: Network Bandwidth/Capacity
Bandwidth is a shared resource
At local level we share the wireless or share a home or office router
However probably, the bottleneck is likely to be upstream to our ISP
ISP have intra-ISP bottlenecks
The destination site (BBC, Facebook) might have inbound capacity limits

## Slide 33: Loss
Another GOLDEN RULE
Packet Loss is a Good Thing
It is the Internet’s defence against failure
Dropping packets (hopefully) causes senders
(processes or users) to rate-limit

## Slide 34: Loss : Network Perspective
Handler
Routing Table
Input Queues
Output Queues
Loss
Notes: Queue is full, packet is dropped

## Slide 35: Packet loss
queue (aka buffer) preceding link has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)

## Slide 36: Throughput : Network Perspective
Throughput : number of bits per time of unit

## Slide 37: Throughput : Network Perspective
Throughput : number of bits per time of unit
Potential Loss and Increased Delay

## Slide 38: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)
server sends bits
(fluid) into pipe

## Slide 39: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
link on end-2-end path that constrains end-2-end throughput, i.e., the smallest/narrowest link
bottleneck link

## Slide 40: STATE OF THE INTERNET

## Slide 41: Bandwidth and Latency: Wired
Broadband is now common in homes
  500Kbps – 1Gbps
  Depends on technology (twisted-pair v. optical)
Offices have always been different
  1Gbps Ethernet, switched (not shared) is common
  Outbound varies enormously
Low Latency

## Slide 42: Bandwidth and Latency: Wireless
2G
  Don’t try, run web or sms-based applications!
3G / 4G
  3G: ~2.4Mbps
  4G: 100Mbps – 1Gbps
802.11a-n, ac
  b: 11 Mbps
  g: 54 Mbps
  n: 74 Mbps
  ac: 150Mbps
Latency is moderate-poor: its shared bandwidth

## Slide 43: Effect of distance on throughput and download times
Based on (Leighton, 2009)